TES

| Instrument | Product Name | Units | Accuracy Abs::Rel | Temporal Resolution | Horizontal Resol.::Cover1 | Vertical Resol.:: Cover |
| --- | --- | --- | --- | --- | --- | --- |
| TES | Level-1B Radiances [@ 10 µm] Temperature Profile | W/m2/sr/cm-1 K | 1%::1% 2 K::1 K | 1/(2 day) 1/(2 day) | 5.3 x 8.5 km::GN 53 x 169 km::GL 5.3 x 8.5 km::GN 53 x 169 km::GL | 2-6 km::0-34 km |
|  | H2O mixing ratio O3 mixing ratio CO mixing ratio CH4 mixing ratio | %v ppbv ppbv ppbv | 3%::3%v 3%::3-20 ppbv 3%::10 ppbv 3%::14 ppbv | 1/(2 day) 1/(2 day) 1/(2 day) 1/(2 day) | 5.3 x 8.5 km::GN 53 x 169 km::GL 5.3 x 8.5 km::GN 53 x 169 km::GL 5.3 x 8.5 km::GN 53 x 169 km::GL 5.3 x 8.5 km::GN 53 x 169 km::GL | 2-6 km::0-34 km 2-6 km::0-34 km 2-6 km::0-34 km 2-6 km::0-34 km |
|  | HNO3 mixing ratio | pptv | 5%::25 pptv | 1/(2 day) | 53 x 169 km::GL | 2-6 km::5-34 km |
|  | Surface Temperature | K | 1 K:: 1 K | 1/(2 day) | 533 x 8.5 km::GN | NA::sfc |
| 1 GN represents Global Coverage (nadir view); GL represents Global Coverage (limb view); 2 NA = not applicable 3 Values for clear skies, northern mid-latitudes & mid-troposphere |

| Product Name | Change | Change Rationale |
| --- | --- | --- |
|  | Was | Is |  |
| HNO3 mixing ratio | 3 pptv | 25 pptv | 25 pptv is sufficient to study HNO3 mixing ratio in polluted environments. 3 pptv volume HNO3 would only be encountered in the cleanest atmospheres of the South Pacific. Measurements at this level would require detector noise that is well beyond the state of the art. |
| H2O/HDO mixing ratio | 0.5-50 ppmv | Deleted | TES was not proposed or designed to make this measurement. This requirement should have been rejected when first proposed. |
| Temporal Resolution | 1/(4 day) | 1/(2day) | Studies published in 1999 and 2000 by M. Luo of the TES Science team show that the change in sampling to 1 day on, 1 day off gives the optimum sampling of temporal and spatial distribution of the TES data products. This change has no impact on average or peak data rates, mechanism usage or lifetime, cost or data processing, and is compatible with the Aura spacecraft operational plan. |
| NO mixing ratio | 15-25 pptv | Deleted | In order to measure tropospheric NO, non-LTE spectral signatures originating in the stratosphere and above must be accurately modeled. At present, the added complexity to TES operational processing is prohibitive, so NO will be pursued as a research product. |
| NO2 Mixing ratio | 500 pptv | Deleted | It was determined several years ago that, for typical humidity profiles, the water vapor continuum overwhelms the NO2 infrared spectrum to the extent that it becomes undetectable below about 13 km. TES will study the possibility of retrieving NO2 under desiccated conditions in the upper troposphere as a research product. Furthermore, OMI has NO2 column as a standard product (measured in a far more favorable spectral region inaccessible to TES) so AURA will still provide an NO2 product. |
| Level 2 detection flags | N/A | Deleted | It had originally been planned to provide a residual (observed – calculated) spectrum over the full frequency range for every scan (4 or 16 seconds). The computational cost of doing this routinely is unacceptable so it is planned to do this no more than once or twice per orbit. Note, however, that the information required to perform this calculation is embedded in the standard products and can be used to generate full residual spectra as needed. |

#### MLS

| Instrument | Product Name | Units | Accuracy Abs::Rel | Temporal Resolution1 | Horizontal Resol.::Cover2 | Vertical Resol.:: Cover |
| --- | --- | --- | --- | --- | --- | --- |
| MLS | MLS Radiances | K | absolute accuracy is 2K or better; precision varies, with -0.01K achieved on long term averages | 2/day [d,n] | 500 km::G | 0.1-1 km::0-90 km |
|  | temperature | K | 1-2K::0.5-1K (5-60 km) | daily (global map) | 500 km::G | 3 km::5-90 km |
|  | geopotential height | m | 30-100 m::10-30 m (10-50 km) | daily (global map) | 500 km::G | 3 km::5-90 km |
|  | cirrus ice content |  | TBD::0.005 g/m3 | monthly (global map) | 200 km::G | 3 km::10-20 km |
|  | H2O concentration | mixing ratio | 5-10%::2-10% (5-80 km) | daily (global map) | 500 km::G | 3 km::5-90 km |
|  | N2O concentration | mixing ratio | 5-10%::0.02-0.05 ppmv (10-60 km) | daily (global map) | 500 km::G | 3 km::10-60 km |
|  | CO concentration | mixing ratio | 5-10%::3-10 ppbv (8-50 km) | monthly (global map) | 500 km::G | 3 km::8-90 km |
|  | O3 concentration (stratosphere) | mixing ratio | 5-10%::2-10% (15-50 km) | daily (global map) | 500 km::G | 3 km::15-90 km |
|  | O3 concentration (troposphere) | mixing ratio | 5-10%::2-10 ppbv (8-15 km) | monthly (global map) | 500 km::G | 3 km::8-15 km |
|  | OH concentration 3 (lower stratosphere) | mixing ratio | 5-10%::0.2-0.5 pptv (18-35 km) | monthly (zonal mean) | 500 km::G | 3 km::18-30 km |
|  | OH concentration 3 (upper stratosphere) | mixing ratio | 5-10%::10% (35-60 km) | daily (global map) | 500 km::G | 3 km::30-80 km |

| Instrument | Product Name | Units | Accuracy Abs::Rel | Temporal Resolution1 | Horizontal Resol.::Cover2 | Vertical Resol.:: Cover |
| --- | --- | --- | --- | --- | --- | --- |
| MLS (cont) | HO2 concentration | mixing ratio | 5-10%::10-50 pptv (20-60 km) | monthly (zonal mean) | 500 km::G | 3 km::20-80 km |
|  | BrO concentration | mixing ratio | 5-10%::3-6 pptv (20-60 km) | monthly (zonal mean) | 500 km::G | 5 km::20-60 km |
|  | ClO concentration | mixing ratio | 5-10%::0.1-0.5 ppbv (15-45 km) | daily (global map) | 500 km::G | 3 km::15-60 km |
|  | HCl concentration | mixing ratio | 5-10%::0.1-0.5 ppbv (10-50 km) | daily (global map) | 500 km::G | 3 km::12-90 km |
|  | HOCl concentration | mixing ratio | 5-10%::0.01-0.03 ppbv (20-50 km) | monthly (zonal mean) | 500 km::G | 3 km::20-50 km |
|  | HNO3 concentration | mixing ratio | 5-10%::0.5-1 ppbv (10-30 km) | daily (global map) | 500 km::G | 3 km::10-50 km |
|  | HCN concentration | mixing ratio | 5-10%::0.01-0.05 ppbv (8-80 km) | daily (zonal mean) | 500 km::G | 5 km::8-80 km |
|  | SO2 concentration3 | mixing ratio | 5-10%::1-2 ppbv (10-30 km) | daily (global map) | 500 km::G | 3 km::10-40 km |
| 1 The temporal resolutions for MLS are valid for both time-sharing (not currently needed) and full-power operating modes; 2 G represents Global Coverage; 3 The SO2 maps will likely be useful only after volcanic eruptions. 3 The Hydroxyl measurement will be made on a best effort basis. |

| Instrument | Product Name | Units | Accuracy Abs::Rel | Temporal Resolution1 | Horizontal Resol.::Cover2 | Vertical Resol.:: Cover |
| --- | --- | --- | --- | --- | --- | --- |
| MLS | MLS Radiances | K | absolute accuracy is 2K or better; precision varies, with -0.01K achieved on long term averages | 2/day [d,n] | 500 km::G | 0.1-1 km::0-90 km |
|  | temperature | K | 1-2K::0.5-1K (5-60 km) | daily (global map) | 500 km::G | 3 km::5-90 km |
|  | geopotential height | m | 30-100 m::10-30 m (10-50 km) | daily (global map) | 500 km::G | 3 km::5-90 km |
|  | cirrus ice content |  | TBD::0.005 g/m3 | monthly (global map) | 200 km::G | 3 km::10-20 km |
|  | H2O concentration | mixing ratio | 5-10%::2-10% (5-80 km) | daily (global map) | 500 km::G | 3 km::5-90 km |
|  | N2O concentration | mixing ratio | 5-10%::0.02-0.05 ppmv (10-60 km) | daily (global map) | 500 km::G | 3 km::10-60 km |
|  | CO concentration | mixing ratio | 5-10%::3-10 ppbv (8-50 km) | monthly (global map) | 500 km::G | 3 km::8-90 km |
|  | O3 concentration (stratosphere) | mixing ratio | 5-10%::2-10% (15-50 km) | daily (global map) | 500 km::G | 3 km::15-90 km |
|  | O3 concentration (troposphere) | mixing ratio | 5-10%::2-10 ppbv (8-15 km) | monthly (global map) | 500 km::G | 3 km::8-15 km |
|  | OH concentration 3 (lower stratosphere) | mixing ratio | 5-10%::0.2-0.5 pptv (18-35 km) | monthly (zonal mean) | 500 km::G | 3 km::18-30 km |
|  | OH concentration 3 (upper stratosphere) | mixing ratio | 5-10%::10% (35-60 km) | daily (global map) | 500 km::G | 3 km::30-80 km |

| Instrument | Product Name | Units | Accuracy Abs::Rel | Temporal Resolution1 | Horizontal Resol.::Cover2 | Vertical Resol.:: Cover |
| --- | --- | --- | --- | --- | --- | --- |
| MLS (cont) | HO2 concentration | mixing ratio | 5-10%::10-50 pptv (20-60 km) | monthly (zonal mean) | 500 km::G | 3 km::20-80 km |
|  | BrO concentration | mixing ratio | 5-10%::3-6 pptv (20-60 km) | monthly (zonal mean) | 500 km::G | 5 km::20-60 km |
|  | ClO concentration | mixing ratio | 5-10%::0.1-0.5 ppbv (15-45 km) | daily (global map) | 500 km::G | 3 km::15-60 km |
|  | HCl concentration | mixing ratio | 5-10%::0.1-0.5 ppbv (10-50 km) | daily (global map) | 500 km::G | 3 km::12-90 km |
|  | HOCl concentration | mixing ratio | 5-10%::0.01-0.03 ppbv (20-50 km) | monthly (zonal mean) | 500 km::G | 3 km::20-50 km |
|  | HNO3 concentration | mixing ratio | 5-10%::0.5-1 ppbv (10-30 km) | daily (global map) | 500 km::G | 3 km::10-50 km |
|  | HCN concentration | mixing ratio | 5-10%::0.01-0.05 ppbv (8-80 km) | daily (zonal mean) | 500 km::G | 5 km::8-80 km |
|  | SO2 concentration3 | mixing ratio | 5-10%::1-2 ppbv (10-30 km) | daily (global map) | 500 km::G | 3 km::10-40 km |
| 1 The temporal resolutions for MLS are valid for both time-sharing (not currently needed) and full-power operating modes; 2 G represents Global Coverage;. 3 The Hydroxyl measurement will be made on a best effort basis. PI Comments MLS absolute accuracy numbers have been changed from generally 3-10% to 5-10%, because 3% absolute accuracy is a stretch - and very difficult (or impossible) to verify. We feel that 5-10% is probably a better number to have as a "requirement", but even 5% will be difficult (and in some cases, impossible) to verify. The overall instrument calibration is at least as good, or better, than the requirements we have consistently put on it, and is *not* the reason for this change. Most other changes actually give *better* results, in some cases significantly so, than the previous table. This is due to the fact that, overall, the instrument performance is better than our requirements, and that our algorithms are generally better now than they were in 1999 when the original table was prepared. Some of the more notable examples, from the "Relative Accuracy (Accuracy Abs::Rel) column of the table, are * HNO3: now 0.5-1 ppbv (10-30 km), was 2-5 ppbv (10-30 km) [factor of 4-5 improvement] * CO: now 3-10 ppbv (8-50 km), was 8-20 ppbv (8-30 km) [factor of 2-4 improvement, and better altitude range] * BrO: upper altitude range extended from 40 km to 60 km Some of the negative changes, indicating poorer advertised poorer advertised performance, and the reasons, are: * Stratospheric O3: now 2-10% (15-50 km), was 0.5-10% (15-50 km) [degraded because our current algorithms are not yet capable of producing 2-10% precision over the altitude range as stated, and we are thus uncomfortable being held to 0.5% precision as a "requirement". Also, 0.5% may have been an error in the initial table. * The highest altitude for vertical coverage has been reduced to 90 km, from 120 km, because we are scanning only up to 90 km (and very briefly, at that) in order to give higher priority of the lower altitudes of more relevance to the Aura mission. * Cirrus ice *absolute* accuracy changed to "TBD", because the ice accuracy depends on the relative number of cirrus ice particles with diameters larger than ~100 micrometers and more in-situ data are needed to establish the climatology for that. |

HIRDLS

| Instrument | Product Name | Units | Accuracy Abs::Rel1 | Temporal Resolution2 | Horizontal Resol4.::Cover3 | Vertical Resol.5:: Cover6 |
| --- | --- | --- | --- | --- | --- | --- |
| HIRDLS | Level-1B Product | W/m2/sr |  |  | 500 km::G |  |
|  | Aerosol Extinction Coef (4 Channels) | /km2 | 210%::2-10% | 2global maps/day | 500 km::G | 1.25km:: 10-30 km 7 |
|  | CFC-11 (CFCl3) concentration | mixing ratio | 4-8%::2-10% | 2global maps/day | 500 km::G | 1.25km:: 7-28 km |
|  | CFC-12 (CF2Cl2) concentration | mixing ratio | 4-8%::1-10% | 2 global maps/day | 500 km::G | 1.25km:: 7-30 km |
|  | CH4 concentration | mixing ratio | 3-5%::3-10% | 2 global maps/day | 500 km::G | 1.25km:: 10-65 km |
|  | ClONO2 | mixing ratio | 5-10%::8-15% | 2 global maps/day | 500 km::G | 1.25km:: 17-40 km |
|  | Cloud Top Height |  | 250m::125m | 2 global maps /day | 500 km::G | 250m:: 7-24 km |
|  | Geopotential Height- Gradient | m/km | 0.04m/km:: 0.04m/km | 2 global maps/day | 500 km::G | NA:: 15-30 km 8 |
|  | H2O concentration | mixing ratio | 3-5%::3-10% | 2 global maps/day | 500 km::G | 1.25km:: 7-70 km |
|  | HNO3 concentration | mixing ratio | 3-5-%::2-10% | 2global maps /day | 500 km::G | 1.25km 10-40 km) |
|  | N2O concentration | mixing ratio | 3-5%::3-10% | 2 global maps / day | 500 km::G | 1.25km:: 10-55 km |
|  | N2O5 concentration | mixing ratio | 5-10%::2-10% | 2global maps/ day [d,n] | 500 km::G | 1.25km:: 20-45 km) |
|  | NO2 | mixing ratio | 3-5%::3-10% | 2 global maps/day [d,n] | 500 km::G | 1.25km:: 20-60 km |
|  | O3 | mixing ratio | 3-5%::1-10% | 2global maps /day | 500 km::G | 1.25km:: 10-80 km |
|  | Temperature/Pressure Profile | K | 7<z<10km 1K::1.5K 10<<50 km 1K::0.5K 50<z<80 km 2.5K::1.5K | 2global maps /day | 500 km::G | 1.25km:: 7-80 km |
| 1 HIRDLS Relative Accuracy –based on a single scan; improved relative accuracy is possible by averaging scans. 2 Two global maps/day means day and night, respectively; 3G represents Global Coverage, 4 Special mode gives 250 x 250 km spacing, for 7 channels (T, O3, H2O, HNO3, aero) 5 Indicated resolution is FOV size of temperature channels, since temperature information goes into retrieval of all other products. Product resolution depends on over-sampling, noise, and data processing, and is expected to be better. 6 Profiles will extend beyond indicated limits, with reduced relative accuracy. 7Altitude range strongly dependent on aerosol loading 8Can be extended hydrostatically from 7-80 km PI Comments: Major change associated with slight FOV increase in the instrument see comment 5. |

OMI

| Instrument | Product Name | Units | Accuracy Abs::Rel 1 | Temporal Resolution | Horizontal Resol.::Cover1 2 | Vertical Resol.:: Cover |
| --- | --- | --- | --- | --- | --- | --- |
| OMI |  |  |  |  |  |  |
|  | Radiances | Watts/cm2/sr | 3%::1% | 1 view/2 sec/once/day | 13 x 24 km::G Daylight | NA |
|  | Total Ozone | DU (3) | 3%::1.5% | once/day | 13 x 24 km::G D | Column |
|  | Ozone Profile | ppmv | 10%::10% | once/day | 13 x 48 km::G Daylight | 6 km::20-45 km |
|  | Tropospheric Column Ozone | DU(3) | 25%::10% | once/day | 52 x 48 km::60S-60N D | Column |
|  | Surface UVB Flux | watt/m2 | 10%::10% | once/day | 13 x 24 km::GD | Surface |
|  | Cloud Scattering Layer Pressure(4) | hPa | 100hPa::30hPa | once/day | 13 x 24 km::D | Surface |
|  | Aerosol Optical Thickness (5) | Dimensionless | 0.1::0.05 30%::10% | once/day | 13 x 24 km::G Daylight | Column |
| 1 Absolute accuracy is given at the horizontal and vertical resolution indicated in the last two columns, and represents the root sum of square of all (1) errors, including forward model, inverse model, and instrument errors, calculated over the covered area, as indicated in the 6th column. Relative accuracy represents a component of the absolute error that varies at the frequency indicated in the 5th column. When multiple values are given the larger value applies. 2 G represents global coverage, D daylight, and V polar vortex conditions; 3 1 DU= 2.687 x 1016 molecules/cm2; 4 Cloud product are limited to optically thick clouds; 5 Aerosol products are limited to cloud-free pixels. |
| OMI (Con’t.) | Aerosol Single Scattering Albedo | Dimensionless | 0.1::0.05 | once/day | 13 x 24 km::GD | Column |
|  | SO2 | mol/cm2 | 3x1016 (50%)::2x1016 (20%) non-volcanic 30%::20% volcanic | once/day | 13 x 24 km::G Daylight | Column |
|  | NO2 | molecules/cm2 | 2x1014::2x1014 background 30%::20% polluted | once/day | 26 x 48 km:GD | Column |
|  | HCHO | molecules/ cm2 | 35%::25% | once/day | 13x24 km::GD | Column |
|  | BrO | molecules/cm2 | 25%::25% | once/day | 13x24 km::GD | Column |
|  | OClO | molecules/cm2 | 15%::10% | once/day | 26x48 km::V | Slant Column |
| 1 Absolute accuracy is given at the horizontal and vertical resolution indicated in the last two columns, and represents the root sum of square of all (1) errors, including forward model, inverse model, and instrument errors, calculated over the covered area, as indicated in the 6th column. Relative accuracy represents a component of the absolute error that varies at the frequency indicated in the 5th column. When multiple values are given the larger value applies. 2 G represents global coverage, D daylight, and V polar vortex conditions; 3 1 DU= 2.687 x 1016 molecules/cm2; 4 Cloud product are limited to optically thick clouds; 5 Aerosol products are limited to cloud-free pixels. PI Comment: Due to the fact that nominal instrument performance was not demonstrated before delivery, because all calibration tests were not completed and calibration analysis is still underway, the level 1b performance, and consequently the quality of the level 2 products, can not be firmly established until the calibration key data base is delivered Dutch Industry. |