Proposal due on 5/14/10

NPP is expected to launch during the periods of performance for the awards solicited under this element, and proposers should plan to profile their work and cost plans to reflect somewhat less intense activity prior to the launch of NPP and during the immediate post-launch instrument check-out period and to reflect greater activity once the SDRs and EDRs are available for evaluation. Proposers also are encouraged to consider proposing as small teams collaborating on the evaluation of groups of related data products if greater efficiency and cost savings might be achieved in doing so.

These properties include, but are not limited to, the temporal and spatial distribution of aerosol optical depth (AOD) and aerosol size. (EDRs: Aerosol Optical Thickness, Aerosol Particle Size, Suspended Matter)

Ozone total column and vertical profile and other atmospheric constituents: Satellite measurements of total column ozone are the global standard for monitoring the response of the ozone layer to the Montreal Protocol mandated reductions in atmospheric chlorine and bromine emissions. The NPP OMPS instruments will continue the ozone data record, started in 1978, by the Total Ozone Mapping Spectrometer (TOMS) series of instruments and carried on by the Ozone Monitoring Instrument (OMI) instrument on EOS Aura. The limb observing component of OMPS will continue the data records of ozone profile observations that started with the Upper Atmosphere Research Satellite (UARS) and were continued by the Microwave Limb Sounder (MLS) instrument on EOS Aura. The changing climate is affecting the speed and timing of ozone layer recovery, adding to the importance of maintaining continuous data records. (EDRs: Ozone Column, Ozone Profile) Evaluation of the OMPS nadir products is being solicited under this program element. Such work could involve comparisons with EOS Aura’s OMI, the European Global Ozone Monitoring Experiment-2 (GOME-2), ground based observations (such as those in the Network for the Detection of Atmosphere Composition Change (NDACC) network), global ozone sondes, etc. OMPS limb EDRs are not being produced by the IDPS because the OMPS limb capability was a late readdition to NPP. Production and evaluation of these products are being covered now by the activities of the NASA SDS Ozone PEATE, NPP Science Team members, and other NASA programs. Successor proposals to continue the NPP Science Team work on OMPS Limb algorithms and data production are welcome under this solicitation.

2.1.2 Calibration and Validation

Some members of the current NPP Science Team have been preparing to provide scientific inputs on, or to make available certain EOS calibration and validation capabilities in support of, critical calibration and validation approaches for science-quality data. Successor proposals in these areas are welcome.

New research activities to add scientific calibration/validation expertise or to complement planned IPO activities for work essential to the evaluation of EDRs will be considered. Proposers must avoid duplicating calibration/validation work that is the responsibility of NGST and the IPO and should offer studies that complement and add value to those efforts while maintaining a tight focus on activities essential for completing the evaluation of the EDRs and/or offering improvements necessary to create an ESDR or CDR. New field validation campaigns will not be considered.

Investigations to explore and demonstrate options for obtaining systematic time series data records that cannot be provided by NPP are sought. Due to performance limitations documented during instrument testing for NPP, a few of the measurements planned are not expected to be of a sufficient quality to usefully extend the current multi-sensor time series. These data products include Ocean Color/Chlorophyll and some aerosol properties (potentially Aerosol Optical Depth) from VIIRS. NASA will continue to evaluate the EDRs for those data products (and such proposals are requested in Section 2.1.1 above) so as to fully document their character and quality and to explore any potential adjustments or algorithmic solutions that might allow for scientific utility. However, NASA is also interested in identifying options to extend these critical time series data products in other ways. In some cases, the performance limitations for an NPP instrument may be mitigated for the instrument version to fly on NPOESS; in these cases there will only be a short potential gap to fill. In other cases, this may not be the case and alternative data sources will be needed for a longer period of time.

Evaluation of Ozone Data Records and other key Atmospheric Constituents from NPP/OMPS,

Using Multi-Angle Spectrally Resolved Retrieval

from a network of Pandora Ground-Based Spectrometer Systems

Proposal Submitted to:

Earth Science Division

##### Science Mission Directorate

NPP SCIENCE TEAM FOR CLIMATE DATA RECORDS

Solicitation: NNH10ZDA001N-NPP

National Aeronautics and Space Administration

Washington D.C.

##### Principal Investigator:

Jay R. Herman

Joint Center for Earth Systens Technology

University of Maryland, Baltimore County

Phone: 301-614-6039

##### Co - Principal Investigator:

Maria Tzortziou

Earth System Science Interdisciplinary Center

University of Maryland, College Park

Phone: 301-614-6048

Co-Investigators

| Co-I | Dr. Nader Abuhassan | University of Maryland, Baltimore County |
| --- | --- | --- |
| Co-I | Dr. Alexander Cede | University of Maryland, College Park |

| TABLE OF CONTENTS (REDO) | page |
| --- | --- |
| ABSTRACT | iii |
| 1. Summary of Personnel and Work Efforts | iv |
| 2. Scientific / Technical / Management Section | 1 |
| 2. 1. Introduction 2. 1. 1. Background---------------------- ------------------------------------------------ 2. 1. 2. Purpose of proposed Research------------------------------------------------ 2. 1. 3. Basis in NRA---------------------------------------------------------------------- 2.1.4 Proposal Objectives And Goals------------------------------------------------- | 1 1 2 3 4 |
| 2. 2. Research Objectives and Work Statement | 6 |
| 2. 3. Technical Approach and Methodology 2. 3. 1. Description of Ground Based Instruments ----------------------------------- 2. 3. 2. Ozone and NO2 Profile Inversion Algorithm -------------------------------- 2. 3. 3. Ozone Retrieval Results -------------------------------------------------------- 2. 3. 4.Profile Retrieval Performance ------------------------------------------------- 2.3.4.1 Ozone retrievals using measured sky radiances ---------------------- 2.3.4.2 Effect of Aerosols on Ozone Profile Retrievals ----------------------- | 7 7 8 10 11 12 13 |
| 2. 4. Summary | 15 |
| 2.5 Impact of proposed work | 15 |
| 2.6 References | 16 |
| 3. Management APPROACH | 18 |
| 4. Facilities and Equipment | 19 |
| 5. Budget Justification | 20 |
| 6. BIOGRAPHICAL SKETCHES | 22 |
| 7. Current & Pending Support | 30 |
| 8. Letters of ComMitment | 30 |

Abstract

Ensuring continuous science-quality satellite data records of tropospheric and stratospheric ozone amounts and vertical distribution is among the key objectives of the National Polar-Orbiting Operational Environmental Satellite System (NPOESS) and the NPOESS Preparatory Project (NPP). Maintaining ozone data continuity is critical not only for monitoring the response of the ozone layer to the Montreal Protocol mandated reductions in atmospheric chlorine and bromine emissions, but also for studying feedbacks between climate change, ozone changes, and air quality. This proposal targets the above NPP mission objective and focuses on the evaluation of the Total Column Ozone environmental data records (EDRs) and Ozone Vertical Profile products that will be derived from both the nadir and limb observing components of the NPP Ozone Mapping and Profiler Suite (OMPS). In addition to ozone, the OMPS system will provide other products useful to the atmospheric community, including amounts of Nitrogen Dioxide (NO2) from biomass burning and urban pollution and aerosol optical thickens and vertical distribution. The innovative aspect of this proposal is that we plan to use a new network of recently developed, highly accurate, extensively tested and validated Pandora ground-based spectrometer systems. The Pandora systems have the capability of providing the needed ground-based information on trace gas (O3, NO2, SO2, HCHO, CHOCHO, H2O) and aerosol variability at the accuracy and temporal/spatial scales required for NPP data validation.

The high sensitivity Pandora CCD system uses a small spectrometer, fiber optic coupled to an optical head and pointing device. The entire spectrometer is kept in a temperature control chamber to improve the precision of the spectral radiance measurements. The proposed retrieval method uses our recently published Multiple-Angle Spectrally Resolved MASR algorithm for measuring stratospheric and tropospheric O3 total column amounts and vertical distribution. Ozone retrievals can be obtained every 10 minutes with an altitude resolution of 2.5 to 3 km starting at the ground using measured direct-sun and sky radiances in the spectral range 280 – 525 nm (spectral resolution of 0.5 nm). The Pandora MASR method is designed as an alternative to balloon sondes or lidars, which are too expensive to obtain diurnal profile data over long periods at multiple sites.

Pandora spectrometers also provide simultaneous measurements of other trace gases and aerosols, information that is critical for accurate ozone profile retrievals. Moreover, the proposed measured correlations between boundary layer O3 and NO2 and HCHO amounts, in combination with the spectrally resolved measurements of aerosol properties in the UV-Visible, will provide a unique dataset that will be used for testing/validating model photochemistry. We are proposing to deploy several existing copies of the Pandora CCD system with high signal to noise ratio (1000:1) needed for O3 and NO2 profile retrievals, at several key locations as needed for capturing satellite sub-pixel and pixel-to-pixel variability. Frequent (10 minutes) ozone and NO2 profiles will insure coincidence with NPP satellite overpass times. The results will be used to validate and improve NPP retrieval algorithms so that the NPP O3 and trace gas retrievals can be used for monitoring the response of the ozone layer to future atmospheric changes, bounding tropospheric photochemical models, and studying the evolution of tropospheric ozone, trace gases, and aerosols and their impacts on climate and air quality.

# 1. Summary of Personnel and Work Efforts

| Name | Time %/Yr | Responsibilities | ORG |
| --- | --- | --- | --- |
| Dr. Jay Herman, PI | 30 | Overall responsibility for management, algorithms, and data analysis. | UMBC |
| Dr. Maria Tzortziou, Co-PI | 33 | Management and Coordination of Efforts, data and radiative transfer analysis, algorithm development. | UMCP |
| Dr. Alexander Cede, Co-I | 33 | Spectrometer scientist | UMCP |
| Dr. Nader Abuhassan, Co-I | 33 | Spectrometer Scientist and Engineer | UMBC |

UMCP		University of Maryland, College Park

UMBC		University of Maryland, Baltimore County

2. Scientific / Technical / Management Section

2. 1. Introduction

This proposal is for the evaluation of the Total Column Ozone environmental data records (EDRs), Ozone Vertical Profile, and NO2 products that will be derived from both the nadir and limb observing components of the NPP Ozone Mapping and Profiler Suite (OMPS) (Fig. 1 Top).

The innovative aspect of this proposal is that we plan to use a network of recently developed, highly accurate, extensively tested and validated Pandora ground-based spectrometer systems (Fig 1 Bottom). Pandora has the capability of providing needed information on trace gas (O3, NO2, SO2, HCHO, CHOCHO, H2O) and aerosol variability at the accuracy and temporal/spatial scales and coverage required for NPP data validation.

Pandora ozone (O3) and nitrogen dioxide (NO2) profile retrievals can be obtained every 10 minutes. Ozone profiles will have an altitude resolution of 2.5 to 3 km starting at the ground using measured direct-sun and sky radiances in the spectral range 280 – 525 nm (spectral resolution of 0.5 nm). NO2 profiles, using the MAXDOAS technique [REF], will have higher resolution, since most of the NO2 is in the boundary layer (1 to 3 km). Existing copies of the Pandora spectrometers will be deployed at key locations to map out the NPP/OMPS sub-pixel and pixel-to-pixel variability, and evaluate and improve the NPP satellite retrievals. Previous methods for determining O3 profiles from ground-based relied on balloon flights or on specially designed lidars. Both of these methods are expensive to use for frequent measurements at multiple sites, and lidar tropospheric ozone profile data cannot be acquired at times corresponding to mid-day NPP satellite overpasses. The retrieval method proposed here is a significant improvement over the above methods, and is based on our recently published [Tzortziou et al., 2008] Multiple-Angle Spectrally Resolved (MASR) retrieval method for measuring stratospheric and tropospheric ozone and trace gas profiles. For both NO2 and O3 profile retrievals, the MASR data will be constrained by direct-sun retrievals of TC (total column) amounts [Cede et al., 2006b; Herman et al., 2008]. A critical element for accurately determining O3 profiles is the simultaneous determination of aerosol optical properties (scattering and absorption). Aerosol properties will be determined simultaneously with the ozone retrieval using both PANDORA and our newly deployed shadowband spectrometer CLEO (300 to 900 nm with 1 nm resolution, see Figure 1 Bottom Left).

2.1.1. Background

Ozone and nitrogen dioxide are critical atmospheric constituents involved in the Ozone and nitrogen dioxide are critical atmospheric constituents involved in the photochemistry of the troposphere and stratosphere. The details of their altitude distributions are vital to understanding boundary layer air quality and photochemistry. Thus, long term, highly accurate and stable satellite observations of total column amounts and vertical distribution of ozone and other atmospheric constituents by the OMPS Nadir and Limb sensors are key objectives expected to be achieved by the NPOESS mission. Evaluation, validation, and improvement of these products is the main objective of our proposal.

In addition to regulating the oxidation capacity of the lower atmosphere and influencing background levels of trace chemicals, O3 is an important greenhouse gas, affecting radiative balance and global climate. Ozone absorption in the UV-B (280 nm <  < 320 nm) region of the solar spectrum affects many photochemical and biological processes as well as shielding the Earth’s surface from UVB radiation. Boundary layer ozone and its chemical reactions with nitrogen oxides are major contributors to urban smog, which continues to pose a health risk to a large percentage of the US population. Nearly 100 major cities in the United States are periodically exposed to concentrations of ozone that exceed EPA health-based air-quality standards. Increased ground-level ozone concentrations are toxic upon inhalation or contact, posing serious threats to agricultural productivity and human health.

One of the main precursors of tropospheric ozone (smog) is NO2, via photochemical reactions with hydrocarbons. Elevated concentrations of NO2 in the boundary layer contribute directly (it is a toxic gas) and indirectly (through particle formation) to adverse health effects including lung damage, increased susceptibility to respiratory illnesses, and aggravation of heart and lung conditions [e.g. Environmental Protection Agency, 1998]. Observations over Boulder and Fritz Peak, Colorado, showed that high concentrations of NO2, due both to pollution and to production by lightning in convective clouds, can reduce downwelling visible radiation by about 5-12% [Solomon et al., 1999], corresponding to an estimated local radiative forcing effect that exceeds that of CO2 [IPCC, 2001].

(a) (b)

Figure 2: Satellite observed spatial variability in (a) smog or tropospheric ozone, and aerosol index (over Indonesia on October 21, 1997) derived by TOMS/TOMS and Terra/MODIS; (b) tropospheric column NO2 (DU) derived from OMI measurements (one year averaged for 2005). NO2 hot-spots coincide approximately with the locations of the labeled cities.

Tropospheric O3 and NO2 amounts are highly variable in time and space (Figure 2), and are influenced by both natural and anthropogenic emissions. Fossil fuel combustion for transportation, industrial activities (power generation) and biomass-burning are the major NO2 sources, contributing about 70% on a regional scale and even more in local urban environments. Understanding the processes that affect O3 and NO2 changes and impacts on air quality, as well as feedbacks on climate change, requires an integrated observational strategy using frequent (e.g. hourly) measurements of the concentrations and vertical distributions of both constituents. Recent analysis of data obtained from space-borne ozone monitoring instruments such as SBUV and AURA-OMI has shown that it is possible to obtain information on O3 vertical distribution, tropospheric NO2, trace gas and aerosol amounts from satellite observations, but with considerable uncertainties. For these data and for NPP/OMPS, ground-based validation is essential to drive improvements in satellite retrieval algorithms. Detailed ground-based O3 and NO2 profile measurements, such as those proposed here, will help validate satellite retrievals,  and quantify the role of both chemical constituents on local and regional environmental degradation, tropospheric chemistry, surface UV-B budgets, human health, and radiative forcing.

Two main techniques have been available for measuring O3 vertical profiles at high vertical resolution: (i) in-situ sensing from balloon sondes and aircraft [e.g. Thompson et al., 2003], and (ii) remote sensing using ozone lidars [e.g. Browell et al., 1985; Uthe et al., 1992, McGee et al., 1995]. However, these measurement approaches are not suited for long-term hourly measurements at multiple sites. Moreover, active ozone-lidar techniques usually do not detect changes in the boundary layer (altitudes below 7 km), and are limited to night, early morning, and late evening observations [McDermid et al., 1995, 2002; McGee et al., 1995]. This makes the lidar technique unsuitable for validating mid-day satellite retrievals of highly variable tropospheric ozone amounts. Several techniques have been developed for obtaining limited tropospheric information from satellites and ground-based observations. The ground-based Umkehr zenith-sky radiance technique [e.g. Mateer, 1965; Petropavlovskih et al., 2005] provides information on stratospheric and limited information on upper tropospheric O3 profiles. While satellite overpasses are midday, Umkehr observations are restricted to measurements near sunrise and sunset (solar zenith angles, SZAs, between 60o and 90o), and last approximately 2 hours, during which significant changes in atmospheric conditions can occur, causing significant retrieval errors.

The proposed MASR method, based on automated passive remote sounding from the ground, is a significant improvement over the Umkehr method, and is designed as an alternative to balloon sondes or lidars, which are too expensive to obtain continuous diurnal profile data over long periods at multiple sites. The MASR algorithm uses an optimal estimation technique [Rodgers, 2000] applied to ground-based observations of sky radiances measured simultaneously at 315 wavelengths (300-340 nm with 0.13 nm steps), multiple viewing zenith angles (0o to 90o), every 10 minutes during the day, to derive high accuracy and high vertical resolution (~2 km in the lower troposphere) trace gas retrievals. Since the wavelength ranges for NO2 (400 nm – 450 nm) and O3 (300 nm – 340 nm) retrievals are independent, the technique can be optimized for retrievals of both O3 and NO2 profiles. Boundary layer NO2 profiles have been obtained by the MAX-DOAS technique [Bruns et al., 2006], which is a subset of our proposed method. The major improvements of the NO2 retrieval method proposed here are the use of more observing angles, the use of the simultaneous direct-sun retrieved value of total column NO2 to constrain the altitude profile retrieval, and the simultaneous information on O3 profiles and aerosol properties. The simultaneous suite of measurements is essential to understand the build up of smog in industrial urban areas.

In addition to O3 and NO2, the Pandora spectrometers provide simultaneous measurements of aerosols, information that is critical for accurate ozone profile retrievals. Moreover, the proposed measured correlations between boundary layer O3 and NO2 and HCHO amounts, in combination with the spectrally resolved measurements of aerosol properties in the UV-Visible, will provide a unique dataset that will be used for testing/validating model photochemistry. We are proposing to deploy several existing copies of the Pandora CCD system with high signal to noise ratio (1000:1) needed for O3 and NO2 profile retrievals, at several key locations as needed for capturing satellite sub-pixel and pixel-to-pixel variability. Frequent (10 minutes) ozone and NO2 profiles will provide a unique dataset for insuring coincidence with NPP satellite overpass times. The results will be used to validate and improve NPP retrieval algorithms so that the NPP O3 and trace gas retrievals can be used for monitoring the response of the ozone layer to future changes, bounding tropospheric photochemical models, and studying the evolution of tropospheric ozone, trace gases, and aerosols and their impacts on climate and air quality.

2.1.2 Relevance to NASA’s Strategic Goals and Basis in specific NRA Solicitation

The research we propose is related to NASA’s strategic goal and Science objective (as stated in the Strategic Plan) to: “Conduct a program of research and technology development to advance Earth observation from space, improve scientific understanding, and demonstrate new technologies with the potential to improve future operational systems”. This proposal addresses the goal through much needed satellite validation of data and algorithms for critical measurements in the troposphere and stratosphere.

This specific NRA solicitation calls for proposals to evaluate “Ozone total column and vertical profile and other atmospheric constituents” derived by NPP/OMPS. According to the specific NRA, “the changing climate is affecting the speed and timing of ozone layer recovery, adding to the importance of maintaining continuous data records. (EDRs: Ozone Column, Ozone Profile) Evaluation of the OMPS nadir products is being solicited under this program element. Such work could involve comparisons with EOS Aura’s OMI, the European Global Ozone Monitoring Experiment-2 (GOME-2), ground based observations, global ozone sondes, etc… Successor proposals to continue the NPP Science Team work on OMPS Limb algorithms and data production are welcome under this solicitation.”

Our proposed measurements of total column and vertical distribution of O3 and NO2 every 10 minutes using a network of accurate ground-based spectrometer systems provide a new capability for validation of the NPP instrument OMPS, both the nadir and limb sensors. This in turn will provide new knowledge for understanding tropospheric composition and the sources driving composition changes in the stratosphere, troposphere, and boundary layer. The proposed measurements are in support of Calibration and Validation efforts during the NPP mission at pre-existing sites where Pandora spectrometers are located. We are not proposing new field campaigns for ozone profile and trace gas validation. As part of the validation effort, we will produce systematic time series of day-to-day diurnal variation that cannot be provided by NPP. We will also provide high quality measurements of aerosol optical properties (optical depth and single scattering albedo) as a function of wavelength, in both the visible and UV wavelength ranges, to extend and validate the measurements expected from VIIRS and OMPS.

The proposed work also fulfills the following NASA objectives, “Atmospheric composition determines air quality and affects weather, climate, and critical constituents such as ozone… NASA’s research for furthering our understanding of atmospheric composition is geared to providing an improved prognostic capability for the recovery of stratospheric ozone and its impacts on surface ultraviolet radiation, the evolution of greenhouse gases and their impacts on climate, and the evolution of tropospheric ozone and aerosols and their impacts on climate and air quality”. The result of this effort will be an automated, passive measurement of diurnal variation of tropospheric O3 and NO2 as a function of altitude from the lower troposphere to the stratosphere. The data (ozone, aerosol, trace gas amounts) will be readily available to NASA and the scientific community for NPP/OMPS validation of retrieved data, for bounding tropospheric photochemical models, and will provide a unique dataset for studying the evolution of tropospheric ozone and aerosols and their impacts on climate and air quality at each location where Pandora spectrometers are deployed.

2. 2. Proposed Research Objectives and Work Statement

The main objective of the proposed project is the implementation of an integrated ground-based measurement program that will provide detailed information on tropospheric and stratospheric O3 and NO2 amounts and their vertical distributions at the accuracy and temporal/spatial scales and coverage required for NPP data validation. The O3 and NO2 profile measurements will be integrated into an ongoing measurement program of trace gas amounts (SO2, NO2, HCHO, CHOCHO, and H2O) and aerosol optical properties (aerosol optical depth AOD and single scattering albedo SSA) from direct-sun viewing spectroscopy.

We are proposing to deploy several existing copies of the Pandora CCD system with high signal to noise ratio (1000:1) needed for O3 and NO2 profile retrievals, at several key locations as needed for capturing satellite sub-pixel and pixel-to-pixel variability. Frequent (10 minutes) ozone and NO2 profiles will provide a unique dataset for insuring coincidence with NPP satellite overpass times. The results will be used to validate and improve NPP retrieval algorithms so that the NPP O3 and trace gas retrievals can be used for monitoring the response of the ozone layer to future changes, bounding tropospheric photochemical models, and studying the evolution of tropospheric ozone, trace gases, and aerosols and their impacts on climate and air quality.

| Year | Statement of Work (Years 1 to 3) |
| --- | --- |
| 1 | Apply the O3 profile retrieval MASR algorithm to PANDORA measured radiances using enhanced aerosol data to optimize the tropospheric profile retrieval capability. Perform validation of the Pandora O3 profile retrievals at GSFC with existing annual balloon ozone-sonde measurements campaigns, and with O3 profile retrievals from our modified Brewer double spectrometer. Apply the Pandora O3 total column and profile measurements for comparison with OMPS and SBUV-2 ozone profile measurements. Apply the enhanced MAX-DOAS technique for the retrieval of tropospheric NO2 altitude profiles and total column amount and compare with NPP and OMI column amounts and SCIAMACHY profile retrievals. Deploy 5 inter-calibrated Pandora systems within an OMPS field of view FOV near GSFC to determine the spatial variability within the FOV Conduct long-term deployment of some calibrated Pandora systems at selected fixed sites near GSFC that are of particular scientific interest (e.g. local urban pollution, coastal marine boundary layer). |
| 2 | Compare the UV and visible aerosol optical depth and single scattering albedo from the operational small aerosol spectrometer shadowband system, CLEO, with aerosol results obtained from NPP/OMPS and VIIRS. Validate the results with PANDORA and AERONET Combine the data from our five operational sites into a regional map of O3 and NO2 spatial variability to estimate the effect of sub-pixel variability on the OMPS retrievals. Since Pandora NO2 retrievals can be performed in the presence of thin clouds, evaluate the effect of clouds in the OMPS field of view on satellite based retrievals of NO2. Use both NPP/OMPS and NOAA/SBUV-2 data for real-time O3 profile comparisons and evaluation of satellite O3 data products (NPP EDRs: Ozone Column, Ozone Profile). |
| 3 | Produce a multi-year data record of comparisons between satellite trace gas total-column and profile retrievals from NPP/OPMS, Aura-OMI and Aura-MLS with ground-based observations from our Pandora network at all five regional sites and at additional sites of particular scientific interest that will exist by year 3 of this proposal. Create a long-term record of diurnal variation of O3 and NO2 profiles, trace gas amounts, and aerosol properties. Publish results on tropospheric NO2 and O3 dynamics, spatio/temporal variability, and evaluation of satellite retrievals. |

Long-term data records of O3 and NO2 profiles, trace-gas amounts, and aerosols from strategic sites will help determine how the atmospheric composition is changing, and how atmospheric trace constituents respond to and affect environmental change. In combination with satellite data, currently by EOS Aura’s OMI and MLS and in the future by NPP/OMPS, the more detailed ground-based measurements will contribute to calculations of radiative forcing needed for estimates of climate change. The measurements will also yield primary data for characterizing air quality at each site.

Ground-based Observations and Algorithms: The instruments we propose to use to address the project’s objectives, are the recently developed Pandora instruments, for determining O3 and NO2 profiles and total column trace gas amounts (O3, NO2, SO2, HCHO, CHOCHO, and H2O) and aerosols from measured sky radiances and direct-sun solar irradiance [Herman et al., 2009], the extensively validated GSFC modified Brewer spectrometer [Cede et al., 2006; Tzortziou et al., 2008], and the CLEO UV-Vis-NIR (300 nm to 800 nm; 1 nm resolution) spectrometer shadow-band type instrument for aerosol optical properties (aerosol optical depth, AOD, and single scattering albedo SSA). We have validated the Pandora measurements using the GSFC modified commercial UV-Vis shadowband [Krotkov et al., XX], the GSFC modified Brewer, and AERONET’s CIMEL sunphotometers. During the period of performance we will use at least five existing sun- and sky-viewing PANDORA CCD spectrometers deployed at strategic sites to provide O3 and NO2 profiling and aerosol capability along with the CLEO spectrometers to provide additional aerosol data.  The derived ozone profiles will also be compared with balloon ozone-sonde measurements during annual campaigns.

The proposed measurement method is based on, and enhances the abilities of, an established O3 profile retrieval technique [Tzortziou et al., 2008]. The MASR method, based on automated passive remote sounding from the ground, is a new alternative to either balloon sondes or lidars. The MASR algorithm uses an optimal estimation technique [Rodgers, 2000] applied to ground-based observations of sky radiances measured at 315 wavelengths (300-340 nm with 0.13 nm steps), multiple viewing zenith angles (0o to 90o), for different solar zenith angles, every 10 minutes during the day. This guarantees coincidence between the ground-based measurements and the NPP/OMPS satellite overpasses. The original retrieval technique was applied to GSFC’s modified ground-based Brewer double spectrometer, where it was developed using 6 wavelengths measured quickly, but sequentially at several view angles. The retrieved O3 profiles have been successfully compared with ozone sondes and satellite data. The use of 315 simultaneously measured wavelengths by Pandora greatly enhances the signal-to-noise ratio SNR, especially by eliminating the effect of atmospheric changes that occur while sequentially measuring single radiances. This results in increased accuracy and vertical resolution (~2 km in the lower troposphere) in a low-cost portable system. Since the wavelength ranges for NO2 (400 nm – 450 nm) and O3 (300 nm – 340 nm) retrievals are independent, the technique can be optimized for retrievals of both O3 and NO2 profiles.

2. 3. Technical Approach and Methodology

2.3.1 Description of Ground Based Instruments

The main instruments we propose to use for continuous evaluation and improvement of the NPP/OMPS retrievals are: (i) our direct-sun and sky-radiance Pandora spectrometer systems (Fig.3) for total column trace gas amounts, NO2, and O3 profile information, (ii) our GSFC (#171) modified Brewer double-grating spectrometer for total column ozone validation (Fig. 4), and (iii) our recently developed CLEO UV-Vis-NIR shadow-band spectrometer for measurements of aerosol optical properties in the UV-Visible spectral range (Fig. 5). The Pandora CCD spectrometer has a 1.6o FOV, and operates from 280 to 525 nm with 0.5 nm resolution with 4 pixels per resolution element. Stray light is reduced for Pandora O3 measurements by blocking visible light using UV bandpass filters. For successful O3 retrieval, both instruments require excellent radiometric and wavelength stability needed to remove the Solar Fraunhofer line structure, which permits the accurate detection of the small residual underlying trace-gas absorption spectra.

The Pandora system consists of an Avantes fiber optic spectrometer with a UV sensitive backthinned 2048 x 16 pixel CCD with two 9-position filter wheels (Open, Opaque, 280-315 nm-Bandpass, 280-380 bandpass, Polarizer-1 Polarizer-2, and Polarizer-3, and three neutral density filters), which is connected to an electronics control box and mounted on a computer controlled sun-tracker and sky-scanner (~0.01 arcsecond pointing accuracy). The opaque position is for the measurement of spectrometer dark current after each measurement. The spectrometer is temperature stabilized (within 0.1oC) inside of a small enclosure. Wavelength calibration and the slit function are determined from lamp emission lines (Hg, Cd, Cu, In, Mg, Zn), three lasers at 325 nm, 442 nm, and 488 nm. Wavelength stability is validated by an analysis of the solar Fraunhofer line structures. Because of stray light at short wavelengths (290-305nm), two UV bandpass filters (280-315 and 280-380 nm with a cutoff at 315 and 380 nm, respectively) are used to greatly reduce stray light.

| Figure 3: Sky-radiance plus direct-sun Pandora (center) and direct-sun only Pandora (right) mounted on a high precision pan and tilt head with 0.01o pointing accuracy. The system, including the portable temperature control chamber (±1oC) is less than $10K to duplicate. The entire system is weather resistant to permit automatic operation. | Figure 4: The modified Mark III Brewer (#171) double spectro-meter, showing the curved radiance entrance port on the lower right to remove the Fresnel polarizing effect. An internal depolarizer is located in front of the grating. | Figure 5: The CLEO optical head, sun-blocking band, and small spectrometer (inset approximately to scale). The final version of CLEO will be smaller. |
| --- | --- | --- |

For total column trace gas amounts (O3, SO2, NO2), Pandora is operated in direct-sun viewing mode using the solar tracker and a sun-centroiding algorithm.  Ozone and NO2 profiles will be retrieved from multiple angle views of sky radiance in the solar principal plane (0o to 90o) and 1731 wavelength steps (300 nm to 525 nm with 0.13 nm steps and 0.4 nm resolution). The O3 and NO2 retrieval algorithms will use a direct optimal estimation radiance fitting technique based on radiative transfer using laboratory measured cross sections.

2.3.2 Total Column O3 and NO2 Retrievals

Total column amounts of O3, NO2 formaldehyde (HCHO) and SO2 derived from direct solar irradiance Pandora measurements in Thessaloniki, Greece are shown in Figure 6, and a second field campaign at Goddard Space Flight Center (GSFC), Greenbelt, Maryland (Figure 7). Two independent instruments, Pandora and MFDOAS, were compared for NO2 at GFSC and found to closely agree [Herman et al., 2009], with both instruments having a clear-sky precision of 0.01 DU (1 DU = 2.67x1016 molecules/cm2) and a nominal accuracy of 0.1 DU. The high precision is obtained from careful laboratory characterization of the spectrometers (temperature sensitivity, slit function, pixel to pixel radiometric calibration, and wavelength calibration), and from sufficient measurement averaging to reduce instrument noise.  The 0.01 DU precision is sufficient to track minute-by-minute changes in total column NO2 throughout each day with typical daytime values ranging from 0.2 to 2 DU.

Since direct-sun measurements can be made in the presence of light to moderate clouds, but with reduced precision (~0.2 DU for moderate cloud cover), a nearly continuous record can be obtained, which is important when matching NPP/OMPS overpass times for satellite data validation.

Figure 6: Fitted Pandora slant column optical depths (blue) for a measurement on July 22, 2006, during the campaign in Greece (red). Left side shows the measurement with the 380nm low pass filter, right side the measurement without filter. Note that the wavelength range 370-380nm appears on both sides. The black legends give the final retrieved vertical column amounts for each atmospheric absorber.

To illustrate satellite validation, comparisons between Pandora and MFDOAS with OMI are shown (Figure 7) for the moderately polluted GSFC site. Similar, but longer-term, comparisons will be made for the Validation of OMPS measured NO2. Knowing the precision and accuracy of the satellite retrievals is essential for the scientific use for air-quality, atmospheric photolysis and chemistry, and for retrieval of other quantities (e.g., accurate atmospheric correction for satellite estimates of ocean reflectance and bio-optical properties).

A direct-sun NO2 inversion method is described in detail in papers by Cede et al. [2006] and Herman et al., [2009]. The biggest advantages of direct-sun measurements are 1) high photon flux (i.e., low noise), 2) simple geometric determination of the air-mass factor (optical path), and 3) no Ring effect or polarization corrections are needed.

The first step in the NO2 retrieval algorithm is to subtract the irradiance logarithm of the measured spectra from the irradiance logarithm of the reference spectrum. Then, a simultaneous least-squares fit is applied to the difference between measured and reference spectra. The fitted functions are a low-order polynomial, the absorption spectra of NO2 and other atmospheric absorbers, and wavelength shift and squeeze functions. The shift and squeeze functions are to provide the best match of the measured spectrum compared to a solar reference spectrum containing the solar Fraunhofer line structure. All the Pandora NO2 retrievals are from a 370 to 500 nm fitting window.  As part of the retrieval of C(NO2), additional trace gas and aerosol amounts are always simultaneously retrieved. Figure xx illustrates the Pandora DOAS retrieval of slant column O3, NO2, HCHO, H2O, and SO2 from clear-sky direct-sun irradiance measurements at Thessaloniki for July 22, 2006. Only a small wavelength shift (0.0016 nm) and squeeze (4x10-6 nm) was needed to match the solar spectrum.

Figure 7: MFDOAS and Pandora NO2 data from GSFC during May 2007. Also shown are the OMI overpass data (green).

In order to obtain absolute NO2 amounts, we use a top of the atmosphere reference spectrum derived from the instrument’s own measurements for two statistical approaches, the “Minimum-Amount Langley-Extrapolation” (MLE) and the “Bootstrap-Estimation” (BE) method [Cede et al., 2006; Herman et al., 2009]. The results are NO2 measurements with a precision of 0.01 DU and an accuracy of 0.1 DU. Cloudy sky precision is reduced to 0.2 DU.

A field campaign at GSFC was designed to compare Pandora with similar measurements made by the MFDOAS spectrometer in a moderately polluted area using the same algorithm, cross sections, and field-calibration methods (Figure xxx). The two independent ground-based spectrometer systems agreed quite well, but the comparison with OMI retrieved data shows some

disagreement. The main reason for this is the high spatial variability of NO2 and the error in OMI retrievals caused by clouds in the OMI field of view 13 x 24 km2. The cloud contamination problem for OMPS will be worse since the FOV is larger. For this reason it is vital to validate the OMPS retrievals and to derive corrections for these retrievals for different sources of error  (clouds, surface reflectivity, and aerosols).

The suite of 5 Pandoras will be used to correct for spatial variability witin a field of view. An example of NO2 temporal variation is shown (Figure xxxx) that leads to spatial variability as the time-varying NO2 plumes are carried by surface winds. These have a typical speed of about 1.5 m/s or 5.4 km per hour. For the particular example, the variation within an OMPS pixel could be 50% of the mean value.

Figure 8: High time variability at GSFC observed by Pandora and MFDOAS. The time resolution of Pandora has now been improved to match MFDOAS.

We can show here some results from the comparisons between Total Column Ozone from Brewer and Pandora

Possibly Reuse this text

The proposed retrieval technique for O3 profiles was originally applied to GSFC’s modified ground-based Brewer double spectrometer [Tzortziou et al., 2008], which allows nearly simultaneous radiance measurements with a 1.5 degree FOV at 6 wavelengths that are about 3 nm apart.

In addition to the higher spectral resolution of the measured radiances and the higher SNR, the portable Pandora spectrometer system has the advantage of being able to measure all wavelengths simultaneously. Previous field experiments have shown that this greatly reduces the measurement noise compared to the Brewer spectrometer [Cede et al., 20xx].

The Pandora system has been operating continuously and successfully since xxx?, providing accurate measurements of total column column NO2 and other trace gases (O3, SO2, HCHO, H2O, O2:O2) and aerosol optical depth (AOD) The results have been validated against the Washington State University MF-DOAS instrument [Herman et al., 2009]. The O3 profiling algorithm, column NO2 algorithm, and comparison with SCIAMACHY and OMI satellite data are discussed in published papers [Liu et al., 2006; Cede et al., 2006b; Tzortziou et al., 2008; Herman et al., 2008].

The Pandora and Brewer measurement datasets consist of: direct-sun irradiances, sky radiances in the principal plane and almucantar. Ancillary data needed for the O3 profile retrieval algorithm (total ozone and aerosol measurements) will be provided from both the CLEO shadowband-type spectrometer and the sky-radiance and direct-sun Pandora spectrometers, along with co-located AERONET Cimel sunphotometers [Holben et al., 1998]) that will provide additional aerosol information (e.g. AOT, particle size distribution (PSD) and SSA at visible wavelengths > 440 nm) [e.g. Dubovik et al., 2002].

2.3.3. Ozone and NO2 Profile Inversion Algorithms

The inversion strategy for O3 profile retrieval uses a vector multiple scattering forward radiative transfer (RT) model f(x) to simultaneously fit angular and spectral measurements of sky radiance constrained by nearly simultaneous direct-sun total column ozone measurement (TCO). The inversion algorithm is based on the optimal estimation approach [Rodgers, 2000], and uses climatological a-priori O3 profile information [McPeters et al., 2007] to stabilize the retrieval. The basic matrix equations used are:

|  | [1a] [1b] |
| --- | --- |

where: x = [xj] = [ln(j)], is the ozone profile solution vector, defined here as the natural logarithm of the ozone amount, j, in a given layer j

xa is the a-priori ozone profile

(a is the error in the a-priori ozone profile, with covariance matrix Sa

y is the vector containing the measured radiances and total column ozone, TCO

is the error in the measurement vector with covariance matrix Sy

A statistically best solution xo is obtained by minimizing a quadratic cost function (x) (minimum residuals) using Gauss-Newton iterations of a linearized approximation K of the forward model f(x) at each iteration step [Tzortziou et al., 2008].

The mathematical technique for obtaining NO2 profiles is similar to that for O3. The main difference arises from NO2 being mostly in the troposphere except on extremely clean days. This requires that PANDORA measure at more elevation angles near the horizon than are needed for O3 in order to resolve the profile information. This has been described previously in terms of the MAX-DOAS technique [Bruns et al., 2006]. Here this technique will be optimized for the PANDORA data, and the retrieval will be constrained by the direct-sun observation of NO2 column amount. Stratospheric information can only be obtained in the early morning when tropospheric amounts of NO2 are usually small and the total column measurements contain mainly stratospheric amounts of about 0.2 DU (1 DU = 2.67 x 1016 molecules/cm2). Based on averaging kernel studies [Spurr, 2003; Spurr et al., 2005], the inversion technique for NO2 should yield at least 3 pieces of information between 0 and 5 km, which is sufficient to determine the profile shape for polluted regions. Key to the accuracy of this measurement is knowledge of the aerosol optical properties in the 400 nm to 450 nm range, which will be provided by simultaneous measurements using AERONET and CLEO. The following sections give details of the method based on the published O3 profile retrieval paper [Tzortziou et al. 2008].

2.3.3. Ozone Profile Retrievals

We have extended the published 6-wavelength Brewer spectrometer method to the 331-wavelength PANDORA spectrometer. Since PANDORA O3 retrieval data are not yet published, the following discussion is given in terms of the published Brewer spectrometer retrievals (Tzortziou et al., 2008). The biggest differences between the Brewer and PANDORA retrievals are PANDORA’s greatly improved SNR, higher spectral resolution of the measurements, the ability of PANDORA to look closer to the horizon (important for NO2), and approximately double the altitude resolution. Currently, Brewer spectrometer O3 profile retrievals have been obtained at 11 Umkehr layers (5 km each) corresponding to an altitude range of about 0 to 55 km

. The proposed MASR method is a significant improvement over the traditional Umkehr approach for obtaining stratospheric O3 profiles, since each profile measurement takes only two minutes instead of two hours in the Umkehr method. Moreover, Umkehr retrievals are limited near sunrise and sunset, while the MASR retrieved profiles are obtained every 10 minutes throughout the day. The improved time resolution in the MASR method is accomplished by using multiple wavelengths and viewing angles in place of multiple solar zenith angles.

2.3.3.1 Ozone profile retrieval performance

Figure 6: The Air Mass Factor for (a) SZA=45o and (b) SZA= 75o. Results are shown at 312 nm and five VZAs (0, 18, 36, 54, 72). The dotted line is the value of the sec(SZA) path.

Air-Mass Factor (AMF) – When the spectrometer looks at a particular view angle, it measures the slant column amount. The ratio of the slant column to the vertical column is known as the AMF. We have used the AMF concept to examine the sensitivity of the sky radiance measurements to relative changes in ozone amount in a given vertical layer. Calculated AMFs are shown in Figure 6 for Brewer measurements at 312 nm, five viewing zenith angles VZA (0, 18, 36, 54, 72o) and two solar zenith angles SZA (45, 75o).

Results show that zenith sky measurements (VZA=0o) at SZA=45o are most sensitive to O3 changes at an altitude of about 6 km (Fig. 7a). As SZA increases, zenith sky measurements become more sensitive to higher altitudes (data not shown here; see Tzortziou et al., 2008). As the VZA increases, the altitude of maximum AMF decreases and the absolute value of AMF increases, indicating that measurements at large VZAs (i.e. 72o) become increasingly sensitive to O3 changes closer to the surface (Figs. 4a). At higher SZAs (e.g. 75o , Fig. 7b) and VZAs smaller than ~54o, the AMF increases with increasing altitude suggesting that sky-radiance measurements at large solar zenith angles are sensitive to stratospheric O3 changes. Moreover, measurements at large VZAs (e.g. 72o) are equally sensitive to O3 changes in the lower troposphere regardless of SZA. This means that sky-radiance data at different SZAs can provide information on diurnal changes in surface and tropospheric O3 amounts. (e.g. Figs. 8b). The vertical resolution will be improved with PANDORA’s better SNR and increased number of wavelengths.

Figure 7: Averaging Kernels at SZAs (a) 75o and (b) 45o. Umkehr layers are just 5 km thick layers.

Ozone Retrieval Sensitivity - Ozone retrievals were performed at large (75o) and relatively small (45o) SZAs. To demonstrate the sensitivity of the retrieval at different altitudes, simulations were performed for an atmosphere with an assumed “true” O3 vertical distribution that was different from the climatological O3 profile in all Umkehr layers (see Figure. 6). In addition, the simulations included some diurnal variation in the “true” column and tropospheric O3 amounts. Stratospheric O3 in the “true” profiles was kept constant throughout the day. The retrieval results were consistent with expectations based on the results of AMF and averaging kernel calculations.

For the retrieval at SZA=75o (Fig. 6a), a climatological O3 profile was used as a-priori information (dashed line in Figure. 6a). The retrieved O3 values in Umkehr layers 3 through 9 (15 to 45 km) were in good agreement with the “true” O3 as expected based on the AMF and Averaging Kernel analyses. These results show that at large SZAs, the retrieval method provides an improved alternative to the traditional Umkehr technique [Mateer, 1965; Petropavlovskih et al., 2005]. The two improvements are: (i) that the measurement only takes a few minutes, and (ii) that the retrieval has better vertical resolution in the lower stratosphere (i.e. Umkehr layer 3). In addition, the SZA=75o retrieval at Umkehr layer 0 was in good agreement with the “true” O3 at SZA=75o showing that measurements at large SZAs can also provide accurate tropospheric O3  retrievals.

Figure 8: Brewer O3 profile retrieval (sza=75) for 23 July 2005 (a) for the real atmosphere with aerosols and (b) for a pure Rayleigh atmosphere. The SBUV2 O3 profile and the ozonesonde measurement are also shown.

Since retrievals at SZA=45o (Fig. 6b) are not sensitive to the stratospheric amount, the retrieval at SZA=75o was used as a-priori information to constrain O3 at high altitudes. Retrieved O3 values were in good agreement with the “true” O3 close to the ground, despite the fact that the “true” tropospheric O3 at SZA=45o was considerably different than that at SZA=75o because of diurnal variation of O3.

2.3.3.2 Ozone retrievals using measured sky radiances

In addition to the studies using synthetic datasets, we applied our retrieval to measured radiances obtained by GSFC’s modified double Brewer spectrometer. The retrievals are shown below for data collected under cloud-free conditions on 23 July 2005. Brewer total column ozone TCO during that day varied between 312 and 323 DU. The satellite SBUV TCO, measured the same day over GSFC (SZA=34o), was 312 DU. Climatological O3 data for July and the latitude zone 30-40o N was used as a-priori information for the retrieval at SZA=75o. The O3 profile retrieved from measurements at SZA=75o was then used as a-priori for the retrievals at smaller SZAs. RT model calculations were performed for radiances at exact values of measured Brewer wavelengths, SZAs, and VZAs to avoid look-up table interpolation errors.

The O3 profiles retrieved (after accounting for the effects of aerosols on the solar principle plane radiance distributions) are shown in Figure 8a for SZA=75o. Estimated O3 amounts in the upper troposphere and in the stratosphere were in good agreement with the SBUV measurements. The retrieved O3 amount in Umkehr layer 0 was 29 DU at SZA=75o. This is consistent with ozonesonde measurements performed at nearby Beltsville, MD, which showed that O3 amount at Umkehr layer 0 was 29DU and 30 DU on 21 and 26 July 2005, respectively (there were no ozonesonde measurements made on 23 July 2005). However, the SBUV O3 value at Umkehr layer 0 was 22 DU, considerably lower than the ozonesonde measurements.

The effect of aerosols on O3 profile retrievals is shown in Figure 9 for both measured radiances (9a) and simulated radiances (9b). Before correction for aerosols, the residuals in equation 1 show a strong dependence on VZA. After correction, the VZA dependence is almost completely removed.  Neglecting the effect of aerosols in the retrieval, resulted in incorrect O3 profiles that were considerably different than the SBUV-2 measured O3 profile both in the troposphere (e.g. Umkehr layer 0) and in the stratosphere (Fig. 8b).

2.3.3.3 Effect of Aerosols on Ozone Profile Retrievals

Figure 9: Residuals in N values (for different vertical angles (zenith (0o) on the left, to 72o on the right) and wavelengths) (a) between Brewer data and model calculations without correction for aerosols; (b) between simulated Brewer data for an atmosphere that included aerosols and model estimations without correction for aerosol effect; (c) between Brewer data and model estimations after correcting for the effect of aerosols. Note, a change of 1 N-value ~ 2.3% in measured – modeled radiances.

Accounting for the aerosol effect in the O3 profile retrieval by using aerosol information from co-located AERONET Cimel sunphotometers and UV-shadowband instruments improved the residuals (both N-values and radiance ratios) (Fig. 8-bottom). These results show that incorporation of an aerosol correction based on co-located aerosol data is necessary for removing the large effect of even small aerosol amounts when retrieving O3 profiles from measurements of sky radiances. Detailed results on the sensitivity of the O3 retrieval to aerosol model (aerosol optical thickness, single scattering albedo, particle size distribution, and aerosol plume height) are presented in Tzortziou et al. [2008].

Do we have ANY results showing NO2 profile retrievals???

We have to talk to Alex

2.4 Summary

The proposed work is to provide the capability for O3 and NO2 profile retrievals at least every 10 minutes throughout each day for the purpose of comparing with and validating NPP retrievals. The ground-based retrievals will use the accurate PANDORA sun-sky observing spectrometers at multiple sites combined with aerosol measurements that are essential for the profile retrieval.  The goal is to obtain a multi-year record that can be used for NPP/OMPS data validation. It will also show the diurnal, daily, and seasonal variations in tropospheric profiles of these critically important atmospheric constituents and the twice daily and seasonal variation in stratospheric ozone profiles using autonomous passive remote sensing. AURA/OMI and SBUV-2 data will be used as test cases for NPP/OMPS data validation.

The profile retrieval method presented in this proposal is based on our previously published papers for O3 profiles and aerosols and trace gases [Liu et al., 2006; Cede et al., 2006a,b; Tzortziou et al., 2008; Herman et al., 2008].

The main purpose of the proposed work is to use the ground-based atmospheric ozone and NO2 profile data to validate satellite retrievals tropospheric and stratospheric ozone profiles and NO2 profiles every 10 minutes that can be used to match the satellite overpass time.

2.5  IMPACT OF THE PROPOSED WORK   (is this needed?????)

This is from the old proposal

The results from this work will be the first remote sensing passive simultaneous retrieval of the diurnal changes in tropospheric O3 and NO2 profiles, other trace gas amounts, and aerosol properties. The retrievals will provide the first practical technique for diurnal profile measurements of tropospheric NO2 and O3 every day, along with simultaneous retrievals of stratospheric ozone, aerosols and trace gases, at a number of sites in the US and worldwide, both over land and over the ocean. Among our study sites will be sites collocated with AERONET, for measurements in conjunction with existing CIMEL sunphotometers, as well as sites where data coverage needed for satellite retrieval validation (or application of tropospheric photochemical models) is currently extremely sparse (e.g. South America). The proposed work will also develop the capability for O3 and NO2 profile (as well as aerosol characteristics) measurements over oceans, where there is almost no data available.

Deployment of the CCD instrumentation and application of the profile retrieval technique will lead to a network of stations suitable for understanding the interaction between diurnally varying tropospheric ozone, NO2 amounts, and aerosols under different local conditions (e.g. high pollution, smoke fires dust events). Incorporation of these results into atmospheric chemistry models will place constraints on the dynamics and chemistry rates, especially the tropospheric photolysis rates such as JNO2. The results will provide much needed validation of the current AURA/OMI and future NPOESS ozone profiling and trace gas measurements. The diurnal measurement capability will provide the only practical method of comparing retrievals from morning and afternoon satellites over multiple sites. The retrieval of trace gas, ozone, and aerosol absorption can be used for an improved atmospheric correction for satellite estimated water-leaving radiances, as needed for improved retrievals of biogeochemical variables especially in coastal regions.

2.6 References

Ahmad Z, C.R. McClain, J.R. Herman, B. Franz, E. Kwiatkowska, W. Robinson, E.J. Bucsela, and M. Tzortziou, 2007, Atmospheric correction for NO2 absorption in retrieving water-leaving reflectances from the SeaWiFS and MODIS measurements”. Applied Optics (Laser, Photonics, and Environmental Optics), 46(26): 6504-6512.

Bates, D.R., Rayleigh Scattering by Air, Planet. Sp. Sci., 32, 785-790, 1984.

Browell, E., S. Ismail, and S. Shipley (1985), Ultraviolet DIAL measurements of O3 profiles in regions of spatially inhomogeneous aerosols. Appl. Opt., 24(17), 2827–2836.

Bruns, M., S. A. Buehler, J. P. Burrows1, A. Richter1, A. Rozanov1, P. Wang, K. P. Heue, U. Platt, I. Pundt, And T. Wagner, No2 Profile Retrieval Using Airborne Multi Axis Uv-Visible Skylight Absorption Measurements Over Central Europe, Atmos. Chem. Phys., 6, 3049-3058, 2006.

Cede, A., and J. Herman, Measurements of O3, SO2, NO2 and HCHO column amounts using a Brewer spectrometer, in Ultraviolet Ground- and Space-based measurements, Models, and Effects V, July 31 to August 1, 2005, San Diego, USA, Proceedings of SPIE Vol. 5886, Pages 7-15, SPIE-The International Society for Optical Engineering, G. Bernhard, J. R. Slusser, J.R. Herman, W. Gao, and G. Bernhard Editors, 2005.

Cede, A., J. Herman, A. Richter, N. Krotkov, and J. Burrows, Measurements of nitrogen dioxide total column amounts using a Brewer double spectrometer in direct Sun mode, J. Geophys. Res., 111, D05304, doi:10.1029/2005JD006585, 2006b.

Cede, A., S. Kazadzis, M. Kowalewski, A. Bais, N. Kouremeti, M. Blumthaler, and J. Herman, Correction of direct irradiance measurements of Brewer spectrophotometers due to the effect of internal polarization, Geophys. Res. Lett., 33 (2), L02806, doi: 10.1029/2005GL024860, 2006a.

Dubovik, O., B. Holben, T. Eck, A. Smirnov, Y. J. Kaufman, M. D. King, D. Tanre, and I. Slutsker (2002), Variability of Absorption and Optical properties of key aerosol types observed in worldwide locations, J. Atmos. Sciences, 59, 590-608.

Environmental Protection Agency, 1998, National air quality and emissions trends report 1997, Research Triangle Park, N. C..

Fishman, J., C. E. Watson, J. C. Larsen, and J. A. Logan (1990), Distribution of tropospheric ozone determined from satellite data, J. Geophys. Res.-Atm., 95 (D4): 3599-3617.

Gao, W., J. Slusser, J. Gibson, G. Scott, D. Bigelow, J. Kerr, and B. McArthur (2001), Direct-Sun column ozone retrieval by the ultraviolet multifilter rotating shadow-band radiometer and comparison with those from Brewer and Dobson spectrophotometers, Applied Optics, 40, (19), 3149-3155.

Guo, X., V. Natraj, D. R. Feldman, R. J. D. Spurr, Run-Lie Shia, S. P. Sander, Y.Yung, Retrieval of ozone profile from ground-based measurements with polarization: A synthetic study, in press, JSQRT, 2006.

Herman, J.R., Elena Spinei, Alexander Cede, George Mount, Thomas. Pongetti, Stanley Sander, Maria Tzortziou, Nader Abuhassan, NO2 Column Amounts from Direct-Sun DOAS Technique and Ground-based PAN-1 MF-DOAS, and FTUVS Spectrometers; Intercomparisons and Application to OMI Validation, in preparation, 2008.

Holben, B. N., T. F. Eck, I. Slutsker, D. Tanre, J. P. Buis, A. Setzer, E. Vermote, J. A. Reagan, Y. Kaufman, T. Nakajima, F. Lavenu, I. Jankowiak, and A. Smirnov (1998), AERONET - A federated instrument network and data archive for aerosol characterization, Rem. Sens. Environ., 66, 1-16.

Hoogen, R., V. V. Rozanov, K. Bramstedt, K. U. Eichmann, M. Weber, and J. P. Burrows (1999), O3 profiles from GOME satellite data-I: Comparison with ozonesonde measurements, Physics and Chemistry of the Earth Part C – Solar-Terrestrial and Planetary Science 24 (5), 447-452.

Intergovernmental Panel on Climate Change (IPCC), 2001, Summary for policy makers, in Climate Change 2001: The Scientific Basis, edited by J. T. Houghton et al., 8 pp., Cambridge Univ. Press, New York.

Krotkov, N., J. Herman, A. Cede, G. Labow (2005), Partitioning between aerosol and NO2 absorption in the UVA, in Ultraviolet Ground- and Space-based Measurements, Models, and Effects V, edited by Germar Bernhard, James R. Slusser, Jay R. Herman, Wei Gao, Proceedings of SPIE, 5886,  (SPIE , Bellingham, WA, 2005), 588601, 2005c

Krotkov, N.A., P.K. Bhartia, J.Herman, Jim Slusser, G. Scott, G. Janson,  G. Labow, T. Eck, and B. Holben, Aerosol UV absorption experiment (2002 to 2004): 1. UV-MFRSR calibration and intercomparison with CIMEL sunphotometers, Opt. Eng., 44 (4), Opt. Eng., 44 (4), 141004, doi:10.1117/1.1886818, 2005a.

Krotkov, N.A., P.K. Bhartia, J.Herman, Jim Slusser, G. Scott, G. Labow, A. Vasilkov, T. Eck, O. Dubovik, and B. Holben, Aerosol UV absorption experiment (2002 04): 2. Absorption optical thickness, refractive index, and single scattering albedo, Opt. Eng., 44(4), 041005, doi:10.1117/1.1886819, 2005b.

Krotkov,N.A., P. K. Bhartia, J. R. Herman, V. Fioletov, and J. Kerr, Satellite estimation of spectral surface UV irradiance in the presence of tropospheric aerosols 1. Cloud-free case, J. Geophys. Res. 103(D8), 8779-8793, 1998.

Liu, X., C. E. Sioris, K. Chance, T. P. Kurosu, M. J. Newchurch, R. V. Martin, and P. I. Palmer (2005), Mapping tropospheric ozone profiles from an airborne ultraviolet–visible spectrometer, Applied Optics, 44, 3312-3319.

Liu, X., K. Chance, and T. P. Kurosu (2007), Improved ozone profile retrievals from GOME data with degradation correction in reflectance, Atmos. Chem. Phys. Discuss., 7, 1575-1583.

Mateer, C. L. (1965), On the information content of Umkehr observations, J. Atmos. Sci., 22, 370-381.

McDermid, I. S., T. D. Walsh, A. Deslis, and M. L. White (1995), Optical-systems design for a stratospheric lidar system. Appl. Opt. 34 (27), 6201-6210.

McGee, T. J., M. R. Gross, U. N. Singh, J. J. Butler, and P. E. Kimvilakani (1995), Improved statrospheric ozone lidar, Opt. Engineering 34(5), 1421-1430.

McPeters R.D., Labow G.J., Logan J.A., Ozone Climatological Profiles for Satellite Retrieval Algorithms, JGR, in press, 2006.

Palm, M., C. von Savigny, T. Warneke, V. Velazco, J. Notholt, K. Kunzi, J. Burrows, and O. Schrems (2005), Intercomparison of O3 profiles observed by SCIAMACHY and ground based microwave instruments, Atmosph.c Chem. and Phys., 5, 2091-2098.

Petropavlovskikh I., P. K. Bhartia, J. DeLuisi, New Umkehr ozone profile retrieval algorithm optimized for climatological studies, Geophys. Res. Lett., 32, L16808, doi:10.1029/2005GL023323, 2005.

Rault, D. F. , Ozone profile retrieval from Stratospheric Aerosol and Gas Experiment (SAGE III) limb scatter measurements, J. Geophys. Res., 110, D09309, doi:10.1029/2004JD004970, 2005.

Rodgers, C, Inverse methods for Atmospheric Sounding: Theory and Practice, World Scientific Publishing Company, 2000.

Schoeberl, M. R., A. R. Douglass, E. Hilsenrath, P. K. Bhartia, R. Beer, J. Barnett, J. W. Waters, M. Gunson,  L. Froidevaux, J. C. Gille, J. J. Barnett, P. F. Levelt,  and P. DeCola (2006), Overview of the EOS Aura Mission, IEEE Trans., Geoscience and Remote Sensing, 44, 5, 1066-1074, 10.1109/TGRS.2005.861950.

Slusser, J. R., D. Kolinski, W. F. Mou, G. Koenig, J. H. Gibson, and D. S. Bigelow (1999), Comparison of column ozone retrievals from 3 different ground-based spectral measurements, Appl. Opt., 38, 1543-1551.

Solomon, S., R. W. Portmann, R. W. Sanders, J. S. Daniel, W. Madsen, B. Bartram, and E. G. Dutton, 1999, On the role of nitrogen dioxide in the absorption of solar radiation, J. Geophys. Res., 104(D10), 12,047– 12,058.

Spurr, R., D. Loyola, W. Thomas, W. Balzer, E. Mikusch, B. Aberle, S. Slijkhuis, T. Ruppert, M. Van Roozendael, J.-C. Lambert, and T. V. Soebijanta, GOME Level 1-to-2 Data Processor Version 3.0: A Major Upgrade of the GOME/ERS-2 Total Ozone Retrieval Algorithm, Applied Optics, 2005.

Spurr, R., LIDORT V2PLUS: a comprehensive radiative transfer package for nadir viewing spectrometers, remote Sensing of clouds and atmosphere, Proceedings SPIE conference 5235, Barcelona, Spain, 2003.

Taubman, B. F., J. C. Hains, A. M. Thompson, L. T. Marufu, B. G. Doddridge, J. W. Stehr, C. A. Piety, and R. R. Dickerson (2006),  Aircraft vertical profiles of trace gas and aerosol pollution over the mid-Atlantic United States: Statistics and meteorological cluster analysis, J. Geophys. Res, 111, D10S07, doi:10.1029/2005JD006196.

Thompson, A. M., J. C. Witte, S. J. Oltmans, F. J. Schmidlin, J. A. Logan, M. Fujiwara, V. W. J. H. Kirchhoff, F. Posny, G. J. R. Coetzee, B. Hoegger, S. Kawakami, T. Ogawa, J. P. F. Fortuin, and H. M. Kelder (2003), Southern Hemisphere Additional Ozonesondes (SHADOZ) 1998-2000 tropical ozone climatology 2. Tropospheric variability and the zonal wave-one, J. Geophys. Res., 108, D2,8241, doi: 10.1029/2002JD002241.

Tzortziou, M., N. A. Krotkov, A. Cede, J. R Herman, and A. Vasilkov (2008), A new technique for retrieval of tropospheric and stratospheric ozone profiles using sky radiance measurements at multiple view angles: Application to a Brewer spectrometer, J. Geophys. Res., 113, D06304, doi:10.1029/2007JD009093.

Uthe, E., J. Livingston, and N. Nielsen (1992), Airborne lidar mapping of ozone concentrations during the Lake Michigan ozone study. J. Air Waste Manage. Assoc., 42,1313–1318.

WMO, Report of the International Ozone Trends Panel 1988, Global ozone research and monitoring project, Report No 18, Chapter 3: Information content of ozone retrieval algorithms. Panel Members: C. Rodgers (Chair), P.K. Bhartia, W.P. Chu, R. Curran, J. DeLuisi, J. Gille, R. Hudson, C. Mateer, D. Rusch, R.J. Thomas, R. Turco, W Wiscombe.

Ziemke, J. R., S. Chandra, B. N. Duncan, L. Froidevaux, P. K. Bhartia, P. F. Levelt, and J. W. Waters (2006), Tropospheric ozone determined from Aura OMI and MLS: Evaluation of measurements and comparison with the Global Modeling Initiative's Chemical Transport Model, J. Geophys. Res., 111, D19303, doi:10.1029/2006JD007089.

3. Management Approach

Dr. Jay Herman, PI    Dr. Herman will be responsible for algorithms, instrument operation, data acquisition, and validation of AURA trace gas (NO2, SO2, O3) amounts, aerosol properties, and UV irradiance and the overall management of the project.  This will include the arrangements for remote site campaigns and coordination with other ongoing AURA validation and science team projects. He will make arrangements for getting other sites to install the modifications to their Brewer spectrometers, arrange support for installation and inversion algorithms, and organize joint measuring programs for satellite validation. Dr. Herman will be responsible for archiving all data and data analysis, and making it available to the AURA science team and other interested investigators. He will also write at least one refereed journal publication on the results of the proposed study.

# Dr. Maria Tzortziou, Co-PI    Dr Tzortziou will share responsibility for project management and coordination of efforts with Dr Jay Herman. She will also be responsible for the theoretical and practical development and optimization of the tropospheric/stratospheric O3 retrieval algorithm.  She will be responsible for performing the data inversions to derive simultaneous solutions for hourly values of tropospheric and stratospheric ozone, NO2, aerosols, and other trace gases from the small spectrometers.

Dr. Alexander Cede, CoI     Dr. Cede will be responsible for the operation of the Brewer spectrometer, obtaining and archiving its data, continuing the development of the algorithms and error analysis, and arranging for data acquisition such that comparison with AURA data is optimum. Dr. Cede will be responsible for acquiring the trace gas amounts of NO2, SO2, and O3. Working with other CoI’s, he will combine the Brewer data with the UV-MFRSR and CLEO data to internally verify the measured aerosol properties and ozone amounts.  In addition, he will help calibrate and analyze the data from the CCD instrument and compare with Brewer data.

Dr. Nader Abuhassan, CoI  Dr. Abuhassan will be responsible for completing the development of the small spectrometer hardware and control software so that a complete temperature controlled operating system is available.  He will then be responsible for building the 3 final operating versions of the small spectrometer based on the existing prototype.  Dr. Abuhassan will also participate in the data analysis of the measured spectra so as to produce tropospheric and stratospheric ozone values and trace gas amounts. He will also acquire the CIMEL and MPL data as processed by AERONET and MPLNET, and make sure that the data quality is good.

# 4. Facilities and Equipment

We currently have a modified double Brewer with 4 years of field use since the modifications, a modified UV-shadowband (UV-MFRSR) with 2 years of operation, a Cimel sunphotometer with several years of operation, and a completed versions of the small PANDORA spectrometer systems with 1 year of operation.  We have access to the AERONET instruments and facilities.

All four of the instruments we propose to use are calibrated and operating at GSFC. The modifications to the Brewer spectrometer are complete and tested.  The addition of the 440 nm channel to the UV-MFRSR has been completed, tested, and been in operation for over 2 years.

The facilities include calibration laboratories with large spherical diffuse light sources using NIST FEL lamps, laser calibration facilities (HeNe and dye lasers), and various support equipment for calibration.  A small amount of additional laboratory equipment will have to be purchased (~$2000/year) consisting of calibration lamps, small electronics, and small optical components.

We have a 4-KW portable gasoline generator for use at remote sites, if needed, along with portable PC’s suitable for data logging.

Computation facilities include 4 Linux high-speed quad-processor data computer/servers with 28 terabytes of data storage, and several high speed Windows PCs.

5. BUDGET JUSTIFICATION

We are requesting a 4-year budget to validate AURA/OMI, GOME-2, SCIAMACHY, and the future NPOESS/OMPS satellite retrievals of NO2 and O3 altitude profiles using an existing network (5 or more) of small sun and sky viewing spectrometer systems PANDORA. As an essential part of the profile retrieval algorithm, we will measure aerosol properties using PANDORA radiance data. The results will be validated over a wide spectral range by the GSFC developed spectrometer version of a shadowband type instrument, CLEO. The CLEO aerosol results will be used to validate and improve OMI and OMPS retrievals, as well as to fully characterize the absorption properties of the atmosphere in both the UV and visible as needed for photochemical and climate studies.

The major portion of the proposed effort involves the PI, the co-PI and 2 of the Co-I’s. One of the Co-I’s will continue the calibration and testing of the small spectrometers based on an already deployed small spectrometer systems. This includes operating the spectrometer to obtain science data for NO2, ozone and aerosols, and comparison with data obtained from the GSFC Brewer spectrometer, CIMEL sunphotometer, and the commercial UV shadowband instrument. The small spectrometer systems (PANDORA and CLEO) will also be deployed on field campaigns along with the commercial UV Shadowband, and Cimel sunphotometer to further validate the results. The entire team will participate in this effort.  Additional small spectrometer systems will be enhanced and deployed during the 2nd and 3rd year (FY10) for deployment at AERONET and selected sites other than GSFC. At least 1 paper will be published.

5.1 Work Effort

Administrative Support: 0.25 FTE per year.

Personnel and Work Efforts – PI and Co-I for which funding is requested

|  |  |  | Yr-1 | Yr-2 | Yr-3 | Yr-4 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Individual | Role | Institution | Year | Year | Year | Year | Total |
| Dr. Jay Herman | PI | UMBC | 0.33 | 0.33 | 0.33 | 0.33 | 1.32 |
| Dr Maria Tzortziou | Co-PI | UMCP | 0.33 | 0.33 | 0.33 | 0.33 | 1.32 |
| Dr. Alexander Cede | Co-I | UMBC | 0.33 | 0.33 | 0.33 | 0.33 | 1.32 |
| Dr. N. Abuhassan | Co-I | UMBC | 0.33 | 0.33 | 0.33 | 0.33 | 1.32 |
| TBD Technician | Supp. | UMBC | 0.25 | 0.25 | 0.25 | 0.25 | 1.00 |
| Resource Admin | Admin | UMBC | 0.10 | 0.10 | 0.10 | 0.10 | 0.40 |
| Total |  |  | 2.75 | 2.75 | 2.75 | 2.75 | 6.68 |

5.2.	Other Direct Costs: (see Table in 5.6)

a.	Consultants - None.

b.	Equipment – See Chart below

c.	Supplies – The budget includes software in the amount of 2K/year

d.	Travel – Campaign and calibration travel domestic and foreign 25K/Year*

e.	Fabrication – Machine shop and circuit boards: None

f.	Publications – 2 publications/year at about $2500 each

g.	ADP/Computer Services – Nomad

h.	Other Direct Support, SED - the GSFC Sciences and Exploration Directorate provides support for information technology security, local area networks, logistics, administration, and other direct services.  This budget includes requirements to sustain those services, derived by applying a percent to all costs except those related to off-site participants (pass through funding).

- Subawards/Consortium – None

*Travel:  The $25K/Year travel budget is for field campaigns that last from 10 to 30 days and involve 2 to 3 people for each campaign.  It is anticipated that there will be at least one foreign trip per year to sites in Europe, South America, Canada, and Japan, and a calibration trip to Hawaii in conjunction with the AERONET calibration site.  We also anticipate 2 or more domestic campaigns per year to sites in different cities and at an ARM site in conjunction with ozonesonde balloon flight campaign such as those conducted by Prof. Anne Thompson and her SHADOZ project.

5.3.	Facilities and Administrative (F&A) Costs, GSFC - Beginning in FY07, the indirect costs for Facilities, Information Technology (IT), and General and Administrative (G&A) will be administered directly from NASA/HQ.  Beginning in FY08, GSFC’s Research & Development Multiple Support (RDMS) will also be administered directly from NASA/HQ.  These items are therefore excluded from this proposal.

5.4.	Other Applicable Costs: None

5.5.	Proposed Cost Sharing (if any):  None

5.6 Budget Justification: Detail

As required by ROSES-2007 NRA, section IV(iii), the Budget Detail given here is restricted to Other Direct Costs and Other Applicable Costs, and does not specify Total Estimated Cost, Direct Labor costs, or Administrative costs.    Fractional ADP costs are now added for NOMAD

6. Biographical Sketches

| RESEARCH AREA EXPERIENCE: | Ion chemistry, earth ionosphere, planetary ionospheres, radio wave propagation in plasmas, stratospheric chemistry and modeling, radiative transfer, atmospheric spectroscopy, uv solar flux measurements, ozone inversion algorithms, and long-term ozone trend analysis, volcanic aerosols, tropospheric trace gas detection, physical oceanography. |
| --- | --- |
| PRESENT POSITION | Principal Investigator Proposed JANUS Mission Project Project Scientist DSCOVR Mission Principal Investigator UV and aerosol from satellite data Principal Investigator Ground-based Measurements Project for UV, Aerosols, and Trace Gases Principal Investigator L-2 SVIP Interferometer/Spectrometer Principal Investigator Ocean Radiation Atmospheric Chemistry and Dynamics Branch, NASA/Goddard Space Flight Center, Code 613.3 Greenbelt, MD 20771 USA |
| EDUCATION: | 1959 - B.S. - Physics, with minor in mathematics, (obtained with high honor) Clarkson College, Potsdam, New York 1963 - M.S. - Physics, Penn. State Univ., State College, PA 1965 - Ph.D. - Physics, Penn. State Univ., State College, PA |
| PREVIOUS POSITIONS: | Principal Investigator for FM-5 TOMS Project Principal Investigator for TOMS/Meteor Project Principal Investigator Atmos. Chem. Model 1960 - 1961 Solid State Devices Engineer, I.B.M., Poughkeepsie, New York 1965 - 1967 National Academy of Sciences Research Associate 1967 - 1970 NASA/GSFC, Ionospheric Physics 1970 - 1975 NASA/GSFC, Planetary Atmospheres, Radiative Transfer 1976 - 1986 NASA/GSFC, Principal Investigator, Stratospheric photochemical modeling and physics. Solar UV Data Analysis, Solar Spectroscopy 1986 - 1990 NASA/GSFC TOMS/SBUV Ozone Data Analysis and TOMS Recalibration 1991 - TOMS Lead Scientist for Data Acquisition and Analysis. |

# Dr Jay R. Herman  PI		(UMBC/GEST)

# RECENT PUBLICATIONS:

- Krotkov, P.K. Bhartia and J.R.Herman, Jim Slusser, Gwen Scott, G. Labow T. F. Eck,and B. N. Holben, UV aerosol absorption experiment (2002-04): 1. UV-MFRSR calibration and performance at GSFC, Optical Engineering 44(4), 041004, 2005.

- Krotkov, P.K. Bhartia and J.R.Herman, Jim Slusser, Gwen, Scott, G. Labow T. F. Eck,and B. N. Holben, Aerosol UV absorption experiment (2002-04): 2. Absorption optical thickness and single scattering albedo, Opt. Eng., 44, 4, 041005, 2005

- Vasilkov, A.P., J.R. Herman, Z. Ahmad, M. Kahru, and G. Mitchell, Assessment of the ultraviolet radiation field in ocean waters from space-based measurements and full radiative transfer calculations, Opt. Eng. 44, 2863-2869, 2005.

- Meloni, D., A. di Sarra, J. R. Herman, F. Monteleone, and S. Piacentino, Comparison of ground-based and TOMS erythemal UV doses at the island of Lampedusa in the period 1998-2003: the role of tropospheric aerosols, J. Geophys. Res., 110, D01202, doi:10.1029/2004JD005283, 2005.

- Tzortziou, Maria, Jay R. Herman, Ajit Subramaniam, Patrick J. Neale, Charles L Gallegos and Lawrence W. Jr Harding, Optical properties and radiation in the Chesapeake Bay estuarine waters:  An in-water optical closure experiment,  J. Geophys. Res., 2005.

- Patra, P.K., S. K. Behera, J. R. Herman, S. Maksyutov, H. Akimoto, T. Yamagata, The Indian summer monsoon rainfall: interplay of coupled dynamics, radiation and cloud microphysics, Atmos. Chem. Phys. Discuss, 5, 2879-2895, 2005.

- Fromm, Michael, R. Bevilacqua, R. Sevranckx, J. Rosen, J.P. Thayer, J. Herman, and D. larko, Pryo-cumulonimbus, injection of smoke to the stratosphere: Observations and impact of a super blowup in northwestern Canada on 3-4 August 1998, J. Geophys. Res., 110, D08205, doi:101029/2004JD005350, 2005.

- Arola, Antti, Stelios Kazadzis, Nickolay Krotkov, Alkis Bais, Julian Grobner, and Jay R. Herman, Assessment of TOMS UV bias due to absorbing aerosols, J. Geophys. Res., VOL. 110, D23211, doi:10.1029/2005JD005913, 2005.

- Tanskanen, A., N. Krotkov, J.R. Herman, and P.K. Bhartia, “A. Arola, Surface UV Irradiance from OMI,  IEEE, TGRS AURA,” special issue, 44, 1267-1271, 2005.

- Cede, Alexander, M. Kowalewski, Stelios Kazadzis, Alkis Bais, Natalia Kouremeti, Mario Blumthaler, and Jay Herman, Solar zenith angle effect for direct-sun measurements of Brewer spectrophotometers due to polarization, Geophysical Research Letters, Vol. 33, L02806, doi:10.1029/2005GL024860, 2006.

- Cede, Alexander, Jay Herman, Andreas Richter, Nickolay Krotkov  and John Burrows, Measurements of Nitrogen Dioxide Total Column Amounts at Goddard Space Flight Center Using a Brewer Spectrometer in Direct Sun Mode, accepted,  Journal Of Geophysical Research, Vol. 111, D05304, doi:10.1029/2005JD006585, 2006.

- Antón, M., V.E. Cachorro, J.M. Vilaplana, N.A. Krotkov, A. Serrano, C. Toledano, B. de la Morena, J.R. Herman, Toms Retrievals Of Erythemal-Cie Uv Irradiance And Daily Cie Doses Compared With Brewer Ground-Based Measurements At El Arenosillo (Spain), submitted JGR as Manuscript # 2006JD007254, 2006.

- Mark O. Wenig, Eric J. Bucsela, Edward A. Celarier, Jim F. Gleason, Alexander M. Cede, Jay R. Herman, Pepijn Veefkind, Ellen Brinksma, Validation Study of Two Years of OMI NO_2 Data, Advanced Environmental Monitoring, 2006.

- Tzortziou M., A. Subramaniam, J. Herman, C. Gallegos, P.Neale, and L. Harding "Remote Sensing Reflectance and Inherent Optical Properties in the Mid Chesapeake Bay", Estuarine, Coastal, and Shelf Science, doi:10.1016/j.ecss.2006.09.018 2006,

- Tzortziou M., J. Herman, C. Gallegos, P.Neale, A. Subramaniam, L. Harding, and Z. Ahmad, "Bio-Optics of the Chesapeake Bay from Measurements and Radiative Transfer Closure", Estuarine Coastal and Shelf Science, 68(2), 348-362, 2006.

- Hsu, N. Christina, Si-Chee Tsay, Michael D. King, and Jay R. Herman, Deep Blue Retrievals of Asian Aerosol Properties During ACE-Asia, IEEE Transactions On Geoscience And Remote Sensing, 44, 3180-3195, 2006.

- Kazantzidis, A. A. F. Bais, J. Grobner, J. R. Herman, S. Kazadzis, N. Krotkov, E. Kyro, P. N. den Outer, K. Garane,  P. Gorts,  K. Lakkala, C. Meleti, H. Slaper, R. B. Tax,  T. Turunen, and C. S. Zerefos., Comparison of satellite-derived UV irradiances with ground-based measurements at four European stations, J. Geophys. Res., 111, D13207, doi:10.1029/2005JD006672, 2006

- Ziauddin, Ahmaad, Charles R. McClain, Jay R. Herman, Bryan A. Franz, Ewa J. Kwiatkowska, Wayne D. Robinson, Eric J. Bucsela, and Maria Tzortziou, Atmospheric Correction For NO2 Absorption In Retrieving Water-Leaving Reflectances From The Seawifs And MODIS Measurements, J. Applied Optics, Accepted, 2007.

- Tzortziou M., A. Subramaniam, J. Herman, C. Gallegos, P.Neale, and L. Harding,  “Remote sensing reflectance and inherent optical properties in the Mid Chesapeake Bay”. Estuarine, Coastal, and Shelf Science, 72(1): 16-32, 2007.

- Tzortziou, M., N. Krotkov, A. Cede, J.R. Herman, and A. Vassilkov, “A new technique for retrieval of tropospheric and stratospheric ozone profiles using sky radiance measurements at multiple view angles – Application to a Brewer”, spectrometer, accepted, J. Geophys. Res., 2007JD009093, 2008.

- Herman, J.R., G. Labow, N.C. Hsu, D. Larko, Changes in Cloud Cover (1998-2006) Derived From Reflectivity Time Series Using SeaWiFS, N7-TOMS, EP-TOMS, SBUV-2, and OMI Radiance Data, accepted, J. Geophys. Res., 2008.

| Dr. Maria Tzortziou, Co-PI (UMCP/ESSIC) |
| --- |
| RESEARCH AREA EXPERIENCE: | Radiative transfer in ocean and atmosphere; Bio-optics of coastal waters; UV, Aerosols, Ozone remote sensing; Remote sensing of Case 2 waters |
| PRESENT POSITION | Research Scientist - Earth Science System Interdisciplinary Center, University of Maryland at College Park |
| EDUCATION: | 1997 B.S. Physics (with high honor), Aristotle University, Greece 1999 M.Sc. Environmental Physics (with high honor), Aristotle University, Greece 2001 M.Sc. Meteorology, University of Maryland College Park (UMCP) 2004 Ph.D. Ocean and Atmospheric Sciences, UMCP |
| PREVIOUS POSITIONS: | 2004-2005 Post-doctoral Fellow - Smithsonian Institution, Smithsonian Environmental Research Center (SERC), MD 1999-2004 Graduate Research Assistant - University of Maryland, UMCP 2001-2003 Pre-doctoral Fellow - Smithsonian Institution, SERC 1998 Visiting Scientist - NASA, Goddard Space Flight Center 1997-1999 Graduate Research Assistant - Aristotle University, Greece, Dept of Physics, Laboratory of Atmospheric Physics. 1996-1997 Research assistant - Aristotle University of Thessaloniki, Dept of Physics, Laboratory of Atmospheric Physics. |
| RECENT PUBLICATIONS | Tzortziou M., N.A. Krotkov, A.Cede, J. R. Herman, A. Vassilkov. "A new technique for retrieval of tropospheric and stratospheric ozone profiles using sky radiance measurements at multiple view angles - Application to a Brewer spectrometer." J. Geophys. Res., 113, D06304, doi:10.1029/2007JD009093 Tzortziou M., J. Herman, C. Gallegos, P.Neale, A. Subramaniam, L. Harding, and Z. Ahmad, “Bio-Optics of the Chesapeake Bay from Measurements and Radiative Transfer Closure”, Estuarine Coastal and Shelf Science, 68,348-362, 2006. Zerefos C, Syrakov D, Ganev K, Vasaras A, Kourtidis K, Tzortziou M, Prodanova M, Dimitrova R, Georgieva E, Yordanov D, and Miloshev N, “Study of the pollution exchange between Bulgaria and northern Greece”, International Journal of Environment and pollution, 22 (1-2): 163-185 2004 Formenti, P., T. Reiner, D. Sprung, M. O. Andreae, M. Wendisch, H. Wex, D. Kindred, K. Dewey, J. Kent, M. Tzortziou, A. Vasaras, and C. Zerefos, “The STAAARTE-MED 1998 summer airborne measurements over the Aegean Sea: I. Aerosol particles and trace gases”, JGR, Vol 107, No D21, 2002 Zerefos C., D. Balis, M. Tzortziou, A. Bais, K. Tourpali C. Meleti, G. Bernhard and J. Herman, "A note on the interannual variations of UV-B erythemal doses and solar irradiance from ground-based and satellite observations", Annales Geophysicae 19: 115-120, 2001 Zerefos C., K. Ganev, K. Kourtidis, M. Tzortziou, A. Vasaras, E. Syrakov, “On the origin of SO2 above Northern Greece”, GRL, Vol. 27, 3, 365-368, 2000 Ahmad Z., Herman J.R.,Vasilkov A., Tzortziou M.,Mitchell G., Kahru M., “Seasonal variation of UV radiation in the ocean under clear and cloudy conditions”, Proc. SPIE Vol. 5156, p. 63-73, UV Ground- and Space-based Measurements, Models, and Effects III; Slusser, Herman & Gao; Eds., 2003. |
| Dr. Nader Abuhassan, CoI |
| RESEARCH AREA EXPERIENCE: | Over 16 years of experience in Industry, National and International Research Centers. Actively participated in the design, development and scientific validation of several instruments and radiation sensors for remote sensing of greenhouse gases and monitoring of atmosphere optical properties. |
| PRESENT POSITION | Sr. Scientist/Engineer at Science Systems & Applications Inc. |
| EDUCATION: | 1991-1995Ph.D. Development of a Portable Multi-spectral Infrared Radiometer, first applications. Department of Physics at the University Pierre and Marie Curie, Paris 6, France (Financial support for the project was provided by the French Space Agency 93/CNES/373 and Cimel Electronique). 1990-1991 DESS Geophysics, (Post Graduate), University Pierre and Marie Curie, Paris6, France. 1986-1987 French language Certification, University of Paris 5 (La Sorbonne), France.Diploma of Electronic Engineering, Damascus University, Faculty of Electrical Engineering, Syria, 1979-1983. |
| PREVIOUS POSITIONS: | 2000- present SSAI Sr. staff Scientist/Engineer supporting the Atmospheric Chemistry &Dynamics branch at NASA/GSFC. 1997-2000 SSAI Sr. staff Scientist/Engineer ­ Sensor Systems supporting the Aeronet Network. at NASA/GSFC. 2000 Ciena Corporation Sr. Engineer ­10GHZ Transceiver. 1991-1997 Cimel Electronique R&D Engineer Paris, France 1988-1990 CNRS visiting Scientist /Engineer at the French National Research Center (CNRS\CRG). |
| RECENT PUBLICATIONS | “Solar Viewing Interferometer Prototype”,Richard G. Lyon, Jay R. Herman,Nader Abuhassan, Cathy T. Marx, Semion Kizhner, Julie Crooke, RonaldToland, Albert Mariano, Cheryl Salerno, Gary Brown, Tony Cazeau, SPIEAstronomical Telescopes and Instrumentation, June 21-25, 2004, Glasgow Scotland. ·Analysis of the performance characteristics of the five-channel Microtops II sun photometer formeasuring Aerosol Optical Thickness and Precipitable Water Vapor.Charles Ichoku , Robert Levy , Yoram J. Kaufman , Lorraine A.Remer , Rong-Rong Li ,Vanderlei J. Martins , Brent N. Holben , NaderAbuhassan, Ilya Slutsker, Thomas F. Eck ,Christophe Pietras , IGR.2001. ·Aerosol optical properties climatology at selected globally distributed sites fromAERONET Holben, B.N., O.Dubovik, A.Smirnov, T.F.Eck, N.Abuhassan,I.Slutsker,W.Newcomb, D.Tanre, Y.Kaufman, N.T.O'Neill, M.King and T.Nakajima, The CCSR COE Symposium/3rd Aerosol-Cloud Remote SensingWorkshop, Kyoto, Japan, December 1-3, 1999. Mineral dust optical properties on the AERONET (Aerosol Robotic Network)sites Smirnov, A., B.N.Holben, O.Dubovik, T.F.Eck, I.Slutsker, andN.Abuhassan,,IGARSS99, Hamburg, Germany, June 26-July 3, 1999. |

| Dr. Alexander Cede, CoI |
| --- |
| RESEARCH AREA EXPERIENCE: | Calibration of (spectro) radiometers, Radiative transfer, UV irradiance at the Earth’s surface, Aerosols, Cloud studies, Atmospheric spectroscopy |
| PRESENT POSITION | Scientist at Science Systems & Applications Inc., since 2002 and now at University of Maryland ESSIC |
| EDUCATION: | 1996 M.S. Physics, University of Innsbruck, Austria 2001 Ph.D. Physics, University of Innsbruck, Austria |
| PREVIOUS POSITIONS: | 1994-1996 Laboratory Assistant at Institute of Medical Physics, University of Innsbruck, Austria 1997-1999 Scholarship of the “Skin Cancer Foundation” of Argentina 2000 Scientist at “Mag. Ing. Schreder – Calibrations, Measurements, Softwaresolutions” 2001-2002 Scientist Institute of Medical Physics, University of Innsbruck, Austria |
| RECENT PUBLICATIONS | Cede, A., and J. Herman, Measurements of O3, SO2, NO2 and HCHO column amounts using a Brewer spectrometer, in Ultraviolet Ground- and Space-based measurements, Models, and Effects V, July 31 to August 1, 2005, San Diego, USA, Proceedings of SPIE Vol. 5886, Pages 7-15, SPIE-The International Society for Optical Engineering, G. Bernhard, J. R. Slusser, J.R. Herman, W. Gao, and G. Bernhard Editors, 2005. Cede, A., S. Kazadzis, M. Kowalewski, A. Bais, N. Kouremeti, M. Blumthaler, and J. Herman, Correction of direct irradiance measurements of Brewer spectrophotometers due to the effect of internal polarization, Geophys. Res. Lett., 33 (2), L02806, doi: 10.1029/2005GL024860, 2006a. Cede, A., J. Herman, A. Richter, N. Krotkov, and J. Burrows, Measurements of nitrogen dioxide total column amounts using a Brewer double spectrometer in direct Sun mode, J. Geophys. Res., 111, D05304, doi:10.1029/2005JD006585, 2006b. Cede, A., B. Bojkov, J. Herman, M. Wenig, E. Bucsela, E. Celarier, and J. Gleason, Validation of OMI Vertical Column NO2 with Brewer Direct Sun Measurements, in preparation, 2006c. Cede, A., E. Luccini, R.D. Piacentini, L. Nuñez, M. Blumthaler, and J. Herman, TOMS-derived erythemal irradiance versus measurements at the stations of the Argentine UV Monitoring Network, J. Geophys. Res., 109 (D8), D08109, 10.1029/2004JD004519, 2004. Cede, A., G. Labow, M. Kowalewski, N. Krotkov and O. Dubovik, Deriving aerosol parameters from absolute UV sky radiance measurements using a Brewer double spectrometer, in Ultraviolet Ground- and Space-based measurements, Models, and Effects III, 4-6 August 2003, San Diego, USA, Proceedings of SPIE Vol. 5156, Pages 323-329, SPIE-The International Society for Optical Engineering, J. R. Slusser, J.R. Herman, and W. Gao Editors, 2003. |

| 7. Current and pending support |
| --- |
| OTHER SUPPORT | Source of Support | Award Amount and Period of Performance | Person-Months and Level of Effort (PM/Year) | Project Title |
| Dr. Herman PI |
| PI Year 4 of 4 | NNH04ZYS004N | $1070K FY2005 to FY2008 | 3 PM/Year | OMI Validation and Analysis of NO2, HCHO, and SO2 |
| PI Year 3 of 3 | NNH04Z YS004N | $706K FY2006 to FY2008 | 3 PM/Year | Ocean Atmospheric Correction 340 – 440 nm |
| PI Year 1 of 5 | NNH06ZDA001N | $2020K FY2008 to FY2012 | 1 PM/Year | Reflectivity Climate Data Record from SBUV, TOMS, SeaWiFS. |
| Dr. Krotkov Co-I |
| Co-I Year 4 of 4 | NNH04ZYS004N | $1070K FY2005 to FY2008 | 3 PM/Year | OMI Validation and Analysis of NO2, HCHO, and SO2 |
| PI Year 2 of 3 | NNH05ZDA001N-AC | $801784 FY2006 to FY2008 | 6 PM/Year | Mapping SO2 emissions with Aura/OMI |
| Dr. Cede Co-I |
| Co-I Year 4 of 4 | NNH04ZYS004N | $1070K FY2005 to FY2008 | 6 PM/Year | OMI Validation and Analysis of NO2, HCHO, and SO2 |
| Dr. Tzortziou Co-I |
| Co-I Year 3 of 3 | NNH04Z YS004N | $706K FY2006 to FY2008 | 6 PM/Year | Ocean Atmospheric Correction 340 – 440 nm |
| Dr. Abuhassan Co-I |
| Co-I Year 4 of 4 | NNH04ZYS004N | $1070K FY2005 to FY2008 | 6 PM/Year | OMI Validation and Analysis of NO2, HCHO, and SO2 |
| Dr Xiong Liu |
|  | N/A |  |  |  |

# Text boxes

Repeated

Replace this figure

I would suggest a different order of results here:

- Results for Total Column Ozone and NO2 (Brewer, Pandora, OMI) (some data from Greece and NEW results)

- Algorithm Description and Results for O3 profiles (comparison Brewer-SBUV2 and ozonesondes)

- Algorithm Description and Results for NO2 profiles? (do we have ANY figures?)

Figure 1: (Top) OMPS sensor suite. (Bottom) Pandora System