## Slide 1: Trend Quality Ozone from the OMPS Nadir Mapper and Nadir Profiler
Rich McPeters1 and Colin Seftor2
Fall AGU, New Orleans December 11, 2017
1NASA Goddard Space Flight Center
2Science Systems Applications Inc.

## Slide 2: The version 2 processing
Improved scattered light and dark current correction
Corrected wavelength registration and bandpass
Calibration adjusted for consistency with SBUV v8.6 time series
Brion/Daumont/Malicet ozone cross sections used
Other instrument artifacts corrected
Goal: data that can be used to continue the MOD long term
Ozone time series
Notes: Especially the dichroic beam splitter

## Slide 3
MOD – Merged Ozone Data: a long term time series created by merging data from a series of UV profiling instruments.
OMPS data will continue the time series

## Slide 4
OMPS data will continue the time series
Notes: N19 orbit near terminator

## Slide 5
OMPS nadir mapper (NM) total column ozone agrees with ground observations to within half a percent, with near zero time dependence.
Notes: Stable to within half a percent

## Slide 6
Nadir Mapper (NM) vs MOD

## Slide 7
Nadir Profiler (NP) vs MOD

## Slide 8
NP profile comparison for one sonde station

## Slide 9
NP profile comparison with NOAA 19 SBUV/2 and MLS

## Slide 11
Tropospheric Ozone
red: OMI total – MLS strat
blue: OMPS NM total – LP strat

## Slide 12: Conclusions
OMPS v2 ozone datasets are trend quality
  NM total column ozone agrees with N19 (-0.2% bias)
  NM ozone agrees with Dobson/Brewer network to within half a percent
  Tropospheric ozone from OMPS agrees well with OMI/MLS ozone
  NP total column ozone has a bias of -1.1%
  NP profile agrees with N19 SBUV and MLS to about ±5%