Version 8 Level-2 Data Record Format

(SBUV channels Shown)

| Word | Content |
| --- | --- |
| 1 | Orbit Number |
| 2 | Greenwich Mean Time seconds |
| 3 | Logical sequence number |
| 4 | Spacecraft altitude (Km) |
| 5 | Day of year |
| 6 | Year |
| 7 | Latitude |
| 8 | Longitude |
| 9 | Solar zenith angle |
| 10 | Solar zenith angle at start of scan |
| 11 | Solar zenith angle at end of scan |
| 12-23 | N256, N274, N283, N288, N292, N298, N302, N306, N313, N318, N331, N340 (Measured n-values from the monochromator) |
| 24-35 | N256, N274, N283, N288, N292, N298, N302, N306, N313, N318, N331, N340 (Measured n-values from the photometer) |
| 36 | Total Ozone |
| 37 | Error flag |
| 38 | Reflectivity |
| 39 | Algorithm flag |
| 40 | Step one ozone |
| 41 | Step two ozone |
| 42-49 | (dN/dΩ)292, (dN/dΩ)298, (dN/dΩ)302, (dN/dΩ)306, (dN/dΩ)313, (dN/dΩ)318, (dN/dΩ)331, (dN/dΩ)340 |
| 50-57 | (dN/dR)292, (dN/dR)298, (dN/dR)302, (dN/dR)306, (dN/dR)313, (dN/dR)318, (dN/dR)331, (dN/dR)340 |
| 58 | (dN/dR)331 (monochromator) for CCR channel |
| 59-66 | Res(N292), Res(N298), Res(N302), Res(N306), Res(N313), Res(N318), Res(N331), Res(N340) |
| 67 | Res(N331) (monochromator) for CCR channel |
| 68 | Terrain Pressure (atm) |
| 69 | Cloud top pressure (atm) |
| 70 | Effective cloud fraction |
| 71 | Snow/Ice Indicator |
| 72 | Ozone below cloud |
| 73 | Surface category |
| 74-76 | Gain1-4, Gain5-8, Gain9-12 |
| 77 | Aerosol Index |
| 78-87 | Layer 0-9 Ozone |
| 88 | Ozone for layer 10 and above |
| 89-98 | Layer 0-9 Efficiency |
| Word | Content |
| 99 | Efficiency for layer 10 and above |
| 100 | Spares |
| 101-121 | 21 layer A-priori ozone profile (DU) (top layer extending to infinity) |
| 122-142 | 21 layer First guess ozone profile (DU) |
| 143-163 | 21 layer Retrieved ozone profile (DU) |
| 164-183 | Estimated error of retrieved profile (%) (top layer not included) |
| 184 | Profile total ozone (DU) |
| 185 | Estimated error of profile total ozone (%) |
| 186-200 | Ozone mixing ratio in prescribed levels (ppmv) |
| 201-215 | Estimated errors in mixing ratio (%) |
| 216-225 | Initial residues (n-value) |
| 226-235 | Final residues (n-value) |
| 236-435 | 10 x 20 Total scattering kernel (top layer not included) |
| 436-445 | Computed single-scattering n-values |
| 446-458 | Input temperature profile in Umkehr layers |
| 459 | Number of iterations for solution convergence |
| 460 | Reflectivity Correction |